1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - BRRRT, Bombs, Rockets, Mavericks

All
- Press B4 to set A/G Master Mode.
- Press Lower Gray Button to cycle selected weapon.
- On Armament control panel (above left knee), station light quadrants mean the following:
  - Top row: left light only = one weapon, both lights = two or more weapons
  - Bottom row: left light = selected station, right light = station empty
- Current weapon information is shown at the bottom left of the HUD.
- "/n" means Mavericks, where n is the number of missiles on each pylon, and the TV display should be on; all the others are self explanatory.
- If weapon text on HUD has a solid box around it, it's in salvo mode (Gray Reset Hat back to toggle) and will drop/shoot from all pylons simultaneously.

BRRRT
1. Press Trigger to BRRRT, works at any time as long as you are in A/G or A/A Master Mode mode.
2. Press Flip-down Trigger to toggle special cannon symbology and PAC (Precision Attitude Control) mode.
  - Note that PAC stabilizes the plane in pitch and decreases sensitivity of elevators, and also keeps plane on target while shooting.
  - Recommended to turn on PAC after rolling in on target, and turn off as soon as you're done shooting.

CCIP bombing
1. Set release mode knob to CCIP (Shift-Gray Reset Hat press, knob is in upper left of cockpit).
2. Set single/ripple and interval:
  1. RELEASE MODE knob is at bottom of Armament Control Panel, above left knee.
  2. Gray Reset Hat forward to turn RELEASE MODE knob, cycles between Single, Pairs, Ripple Single, and Ripple Pairs
  3. Gray Reset Hat backward to toggle Salvo mode (puts a box around the weapon text on the HUD)
  4. If using Ripple mode:
    1. Gray Reset Hat left/right to decrease/increase interval (shown on right side of Armament panel)
    2. Gray Reset Hat press to cycle ripple quantity (shown on left side of Armament panel)
3. Put the thing on the thing and press Red Button to drop.

CCRP bombing
1. Set release mode knob to CCRP (Shift-Gray Reset Hat press, knob is in upper left of cockpit)
2. Designate target visually in the HUD using TDC slew, then TDC press to designate.
3. A few seconds after designating, the designator line disappears and a solid bomb fall line with pipper at the bottom shows.
4. Fly directly at the bomb fall line. The release cue is a small box that starts dropping from the top of the bomb fall line.
5. Bombs will be released automatically (no pickle required) when the release cue reaches the center of the pipper.

Rockets
1. Rockets always fire in CCIP mode.
2. Press Gray Reset Hat back to toggle salvo mode. If weapon text in HUD is not boxed (default), rockets will fire in pairs from opposite pylons. If weapon text is boxed, rockets will fire from all available pylons.
3. Put pipper on the target, press Red Button to fire continuously.

Mavericks
1. TV display will be on when Mavericks are selected.
2. Controls:
  - Slew pipper and TV crosshairs ... TDC ministick
  - Ground lock and begin auto-locking targets ... TDC press
  - Unlock ... Shift-TDC press
  - Re-center pipper on HUD (only when unlocked) ... Middle Finger Hat press
    - Not all Mavs may have a zoomable seeker??
  - Zoom in/out ... Middle Finger Hat up/down
1. When ground locked, Maverick will lock onto targets automatically, will unlock if you slew, and re-lock automatically if you get the crosshairs close to a target.
2. Press Red Button to fire.