501 - A/G - Gun, Unguided Bombs, Rockets

Fence in (switches on lower left instrument panel):
- MASTER ARM ... ARM
- GUN PAC ... ARM
- LASER ... ARM
- TGP ... ARM

Gun -- GAU-8/A 30 mm with 1150 rounds
Combat Mix (CM) load is 5 rounds API, 1 round HEI. HEI load is all HEI.
1. GUN PAC switch ... ARM to use PAC (recommended), GUNARM to not use PAC (left instrument panel)
2. Set SOI to HUD with Coolie Hat up short (Dish Hat up short).
3. Press Master Mode Control Button (Lower Gray Button) to cycle HUD mode to GUNS. Mode is shown in the middle of the HUD.
  - When HUD is SOI, change gun pipper mode with DMS left/right (Middle Finger Hat left/right). The default CCIP reticle (a double ring, where the inner ring unwinds with range) is the most accurate.
1. CCIP pipper shows gun aiming point:
  1. Upper dot in the pipper is AP round impact point, lower dot is HE round impact point.
  2. Small vertical bars inside the CCIP ring are for leading a target moving 20 kts at 90 degrees aspect.
  3. When inner ring starts unwinding, target is at 12,000 ft, then 9 o'clock is 9,000 ft, 6 o'clock is 6,000 ft, 3 o'clock is 3,000 ft.
  4. Range in nmi is shown under the pipper.
    - Tanks: 0.5 to 0.8 nmi and rear aspect or steep dive if possible
    - Light armor: 1.2 nmi
    - Unarmored: 1.5 nmi
1. Trim for level flight for best results.
2. Put the pipper on the target and hold Trigger 1st Stage to activate PAC 1 stabilization. Pipper will be stabilized on the target and pitch sensitivity will be decreased.
3. When pipper is exactly on target, press Trigger 2nd Stage to BRRRRT. PAC 2 stabilization will keep pipper pointed at the target and automatically compensate for recoil.

CCIP bombing
1. On left MFD, go to DSMS page.
2. Select bombs by pressing OSB next to desired pylon(s).
3. Press PROF OSB to go to weapon profile page.
4. Press MODE OSB to cycle CCIP/CCRP
5. Press R1 OSB to cycle SGL/PRS/RIP SGL/RIP PRS.
6. Press R2 OSB to cycle fuzing (for retarded bombs, use Nose for slick, N/T or Tail for retarded)
7. If using ripple:
  1. Enter ripple quantity on UFC scratchpad, then press R3 OSB to set quantity.
  2. Enter interval distance on UFC scratchpad, then press R4 OSB to set interval.
8. (Optional) Change detailed bomb settings by pressing CHG SET OSB, then use UFC scratchpad and OSBs to change settings.
9. Press SAVE OSB to save changes.
10. DSMS page should now show table of weapon profiles.
11. Select profile with up and down arrow OSBs, press ACT PRO OSB to activate.
12. Press Master Mode Control Button (Lower Gray Button) until CCIP shows in HUD.
13. Press Coolie Hat up short (Dish Hat up short) to set SOI to HUD.
14. Put the thing on the thing and press the Red Button.
15. There is also a way to set up CCIP->CCRP release, using the IFFCC switch and a menu that appears in the HUD, see Chuck's.

CCRP bombing -- WIP
1. Designate a target and set SPI to the target.
2. Press Lower Gray Button to cycle HUD to CCRP mode.
3. The bomb fall line will have a small circle at the top. When you get close to the drop point (about 20 seconds, and probably a mile or two depending on altitude and speed), the circle will get a countdown next to it.
4. As the countdown decreases, the small circle will start dropping down the bomb fall line. Press and hold Red Button, bomb releases when the small circle reaches the large pipper (not the velocity vector).

Rockets -- TODO
Basically, follow steps above for CCIP bombing, but select rockets instead.