601 - Notes, Quirks, and Trivia

On MFDs, fields with "[]" can be changed by entering a new value in the UFC scratchpad first, then press the OSB next to the field. Fields with "↕" will cycle through several values when the OSB is pressed multiple times.

General flow for non-gun weapons:
1. Select weapons on DSMS page or by setting SOI to HUD and pressing DMS left/right (Middle Finger Hat left/right).
2. Select CCIP/CCRP mode by pressing Lower Gray Button to cycle HUD mode.
3. Fire with Red Button.

General flow for designating targets:
1. Set SOI to whatever you want to designate with.
2. Press China Hat back short (Rear Thumb Button short) to re-center the sensor on the nose or boresight.
3. Point the sensor at the target.
4. China Hat forward short (Front Thumb Button short) generally toggles FOV.
5. Press TMS forward short (Gray Reset Hat forward short) to lock, and/or TMS forward long (Gray Reset Hat forward long) to set target as SPI.
6. Press China Hat forward long (Front Thumb Button long) to point all sensors at the SPI.
7. SPI cannot be undesignated, only redesignated to a new location??