502 - A/G - LITENING pod TPOD/TGP, LGBs
Not same for A-10C and A-10C II

TGP switch ... ON (left instrument panel), takes 60 seconds to warm up
LASER switch ... ARM (left instrument panel)

Designate a target with TGP
1. On right MFD, go to TGP page either by pressing TGP OSB, or with Coolie Hat right short (Dish Hat right short) to cycle pages.
2. Press Coolie Hat right long (Dish Hat right long) to put SOI in TGP MFD.
3. Controls with TGP as SOI:
  - Slew ... TDC Ministick
  - Zoom ... DMS forward/aft (Middle Finger Hat up/down)
  - FOV toggle ... China Hat forward short (Front Thumb Button press short)
  - Lock target and Point/Area track toggle ... TMS up short (Gray Reset Hat forward short)
  - Set SPI at crosshairs ... TMS up long (Gray Reset Hat forward long)
  - Reset to boresight ... China Hat aft short (Rear Thumb Button press short)
  - Reset to steerpoint ... China Hat aft long (Rear Thumb Button press long)
  - Reset to SPI ... China Hat forward long (Front Thumb Button press long)
  - FLIR/CCD mode ... Boat Switch forward/aft (Pinky Switch down/up) for FLIR BHOT/WHOT, Boat Switch center (Pinky Switch press) for CCD (TV mode).
1. When pointed at the target, press TMS up short (Gray Reset Hat forward short) to set point or area track.
2. Then TMS up long (Gray Reset Hat forward long) to set SPI.

Change laser code and fire laser
1. Change laser code:
  1. Press CNTL OSB.
  2. Enter new laser code in UFC scratchpad, then press L3 OSB to update the laser code.
  3. Press RTN OSB to return to main screen.
2. Toggle firing the laser with NWS button (Flip Down Trigger). On the MFD, "L" will be flashing when laser is firing.
  - (optional) Change NWS button to fire laser only while held or to toggle laser firing with CNTL OSB, LATCH OSB. ON = NWS toggles laser, OFF = laser fires only while NWS is held.

Display
- Below crosshairs is the tracking mode, laser status, and range with range source:
  - Tracking mode: AREA, POINT, INR-A (inertial area, masked), INR-P (ditto, point), or INR
  - Laser status: P=Pointer, L=Laser, B=Both pointer and laser, (T prefix=Training)
    - Flashing laser status letter means laser is firing.
  - Range is slant range to target, and range source is: L=laser range, T=trigonometric range, E=pod is slewing and not tracking a target
- Yardstick number is to the right of the crosshairs, shows distance of right crosshair bar on the ground.
- Bottom of screen shows coordinates of crosshairs. (Format can be changed in CNTL OSB, R2 OSB.)

GBU-12/16/10 LGBs -- WIP needs verification/organization
1. Set up for CCRP bombing as described on other page.
2. Designate a target with the TGP and set as SPI with TMS forward long (Gray Reset Hat forward long).
3. Drop on target as with CCRP mode.
4. Toggle laser firing with Flip-down Trigger press.