504 - A/G - AGM-65 Maverick
Not same for A-10C and A-10C II, or maybe only different for laser mavs?

Fence in (switches on lower left instrument panel):
- MASTER ARM ... ARM
- GUN PAC ... ARM
- LASER ... ARM
- TGP ... ARM

AGM-65D - IR, small warhead
AGM-65G - IR, large warhead
AGM-65H - EO, small warhead
AGM-65K - EO, large warhead
AGB-65L - Laser, large warhead

AGM-65 Mavericks (EO or IR guided) -- WIP
Using Maverick seeker for targeting:
1. (Optional, for decluttering) Put HUD in CCIP mode with Master Mode Control Button (Lower Gray Button). This gives you the small gun cross instead of the large pipper.
2. Select Mavericks in DSMS:
  1. On left MFD, press DSMS OSB.
  2. Press 3 and 9 OSBs (next to Maverick pylons) to select/highlight them.
3. On left MFD, go to MAV page with Coolie Hat left (Dish Hat left) or press MAV OSB.
4. If MFD says OFF at the top right, turn on Mavericks:
  1. Press EO OFF OSB to change to EO ON. Missiles take 3 minutes to cool down. MFD says ALIGN.
  2. When missiles are ready, ALIGN message is replaced with Maverick video feed and HUD goes from ALN to RDY.
5. Press Coolie Hat left long (Dish Hat left long) to set SOI to left MFD (the one with the MAV page). Maverick controls:
  - Toggle Wide/Narrow FOV ... China Hat forward short (Forward Thumb Button press short)
  - Lock target manually... TMS forward short (Gray Reset Hat forward short)
  - Ground lock seeker ... TMS aft short (Gray Reset Hat back short)
  - Unlock/return to boresight ... China Hat back short (Rear Thumb Button press short)
  - Set Maverick target as SPI ... TMS forward long (Gray Reset Hat forward long)
  - Symbology color ... Boat Switch up/down/press (Pinky Switch up/down/press) for black/white/auto.
1. Seeker reticle shows on HUD. Slew onto target with TDC Ministick. It will automatically lock any target inside the tracking gate when it stops slewing.
2. DLZ range indicator is on the lower left of the Maverick MFD.
3. When you have lock (reticle on MFD is "buzzing") and are in range, press Red Button to fire.
  - NOTE Flaps must be up to fire.
Using TPOD for targeting:
1. Follow steps 1-4 above to select and arm missiles.
2. On right MFD, press TGP OSB, then press A-G OSB to select air-to-ground mode.
3. Press Coolie Hat right long (Dish Hat right long) to set SOI to MFD with TGP.
4. Designate target with TGP (see TGP page for full steps).
  1. Slew ... TDC Ministick
  2. Zoom ... DMS forward/aft (Middle Finger Hat up/down)
  3. FOV Wide/Narrow toggle ... China Hat forward short (Front Thumb Button press short)
  4. Lock target, toggle Point/Area track ... TMS up short (Gray Reset Hat forward short)
  5. Set SPI at crosshairs ... TMS up long (Gray Reset Hat forward long)
  6. Reset to boresight ... China Hat aft short (Rear Thumb Button press short)
  7. Reset to steerpoint ... China Hat aft long (Rear Thumb Button press long)
  8. Reset to SPI ... China Hat forward long (Front Thumb Button press long)
  9. FLIR/CCD mode ... Boat Switch forward/aft (Pinky Switch down/up) for FLIR BHOT/WHOT, Boat Switch center (Pinky Switch press) for CCD (TV mode).
5. Set the SPI to the target with TMS up long (Gray Reset Hat forward long).
6. Point all sensors (including the Maverick) at the SPI with China Hat forward long (Front Thumb Button long)
7. Press Coolie Hat left long (Dish Hat left long) to set SOI to MAV MFD for final adjustments.
  - It probably won't be able to lock yet at long range. When you get closer, press TMS up short (Gray Reset Hat forward short) to try to lock the target.
1. DLZ range indicator is on the lower left of the Maverick MFD.
2. When you have lock (reticle on MFD is "buzzing") and are in range, press Red Button to fire.
NOTE Flaps must be up to fire.