301 - Flight - Preflight, Performance Limits
Same as A-10C except turning on HMCS

Preflight (after cold start or from hot start)
1. After arming, load weapons and flight plan into DSMS. On left MFD:
  1. Press LOAD OSB (B3).
  2. Press LOAD ALL OSB (R5).
  3. Reload is complete when * appears next to all items (takes about 20 seconds).
2. Radios ... As needed (left console inboard middle to rear, behind throttle)
3. Lights ... As desired (right console, outboard rear), use Pinky Wheel forward to set "default" lights, Pinky Wheel back to use light panel settings, Pinky Wheel press to turn off all external lights
4. Countermeasures programs ... As desired (see countermeasures kneeboard page for details)
  - If JMR shows OFF on CMSC (under HUD): CMSP JMR switch ... Momentarily forward to set jammer from OFF to SBY (CMSP panel, right console inboard forward, check status on CMSC panel under UFC, should say SBY AIR)
1. Altitude warnings ("Altitude, altitude") ... As desired:
  1. On UFC, press ALT ALRT button to cycle through AGL Floor, MSL Floor, MSL Ceiling. HUD will show current altitude warning and value. Default is 500 ft radar, 0 ft MSL floor, 0 ft MSL ceiling.
  2. Enter new altitude on UFC scratchpad, then press ENT on UFC to set.
2. IFF ... NORM (left console outboard middle, next to throttle)
3. Scorpion HMCS Power switch... ON (right console inboard rear)

Performance limits
- Fuel: 11087 lbs internal
  - with 1x drop tanks (4001 lbs ea.) = 15088 lbs
  - with 2x drop tanks (4001 lbs ea.) = 19090 lbs
  - with 3x drop tanks (4001 lbs ea.) = 23091 lbs
- Flaps: 185 kts (flaps retract automatically so cannot be damaged by overspeed)
- Landing Gear: 250 kts
- Max allowed speed (VNE): 450 kts at sea level
- Stall speed: 120 kts
- Negative G: 10 seconds max, engines will cut due to fuel starvation