304 - Flight - Radios, Countermeasures
Same as A-10C, until ARC-210 is added

Radios
COM1	ARC-186(V)	VHF	36.000 to 76.000 MHz	AM	Aft radio in stack	Comms hat up
COM2	ARC-164	UHF	225.000 to 399.975 MHz	AM	Middle radio in stack	Comms hat down
COM3	ARC-186(V)	VHF	116.000 to 151.975 MHz	FM	Forward radio in stack	Comms hat forward

Powering on:
Set Selector knob to TR (ARC-186(V) or MAIN or BOTH (ARC-164).
Using manual frequencies:
1. Set Selector knob to MAN (ARC-186(V)) or MNL (ARC-164).
2. Set frequency with tuning knobs.
Using preset frequencies:
1. Set Selector knob to PRE (ARC-186(V)) or PRESET (ARC-164).
2. Select preset channel with toothed wheel (ARC-186(V)) or knob (ARC-164).
Changing preset frequencies:
1. Set frequency with tuning knobs.
2. Select preset channel you want to save this frequency to.
3. Press LOAD button (on ARC-164, LOAD button is under the white-labeled flip-up panel).

Countermeasures -- WIP needs verification
- Countermeasures Hat controls:
  - F: 6 Chaff
  - B: 6 Flares
  - U: 1 Flare	L-U: Next program
  - D: 1 Chaff	L-D: Previous program
  - P: Toggle selected program	L-P: Toggle ECM
- Current CM program is shown on the display under the HUD, the letter A-M on the left under CHAFF.
- The CM mode (STBY, MAN, SEMI, AUTO) is shown with the letter under FLARE.
- Change CM program with CM Hat up long or CM Hat down long, or faster by using the NXT rocker switch on the CM panel (left console inboard forward).
- When you change programs, the CM panel will briefly show the settings for the selected program.
- ECM jammer mode is shown on the front panel as AIR, SAM1, SAM2, or AAA. Change with the arrow button next to it.
  - AIR - air-to-air radars
  - SAM1 - single-digit SAMs: SA-2, SA-3, SA-5??, SA-6, SA-8
  - SAM2 - double-digit SAMs: SA-10, SA-11, SA-15, 2S6 (SA-19)
  - AAA - gun systems: ZSU-23-4, Gepard??, M-163 Vulcan??
Default programs:
Prog	Ch	Fl	Int	Cycle
A	2	0	1	10
B	4	0	0.5	10
C	0	4	1	10
D	2	2	1	10
E	2	2	0.5	10
F	4	4	1	10
G	4	4	0.5	10
H	1	0	1	1
I	2	0	1	1
J	0	1	1	1
K	0	2	1	1
L	1	0	1	20
M	0	1	1	20

Change program settings: -- WIP but should be basically accurate
Select a program with CMSP panel (right console inboard forward) NXT rocker switch (Top Hat Ring forward/back) or CM Hat forward long/back long.
  - Selected program is shown in CMSC (under HUD) as the letter under CHAFF.
1. On the CMSP panel (right console inboard forward), set the DISP switch to MENU (forward) to display the current program settings.
2. Press the ^ arrow button below any setting to change it, then use the NXT rocker switch (Top Hat Ring forward/back) to increase/decrease the value.
3. Press RTN button to save.