021 - Cold Start

Cold Start Checklist
1. Throttle ... Idle
2. Canopy ... Open
3. Ground Crew ... Ground Electric Power, ON (Backslash, F8, F2, F1)
4. Starter Switch ... Press (behind throttle)
5. When RPM over 5% ... Throttle to ignition detent (Bottom Thumb Button press)
6. When RPM over 15% ... Throttle to idle detent (Bottom Thumb Button press)
7. When RPM over 40%, Ground Crew ... Ground Electric Supply OFF (Backslash, F8, F2, F2)
8. AFCS Standby switch ... STANDBY (left elbow)
9. ARC-51 UHF Mode knob ... T/R or T/R+G (right console)

Proceed with checklists on next page.