041 - A/A - Radar, Missiles, and Guns
TODO: Test Sight Cage button

Radar
General Info
- Radar azimuth: +/-45 deg (not adjustable)
- Targets can be locked within 10 nmi. TDC cursor only appears when radar is set to 20 nmi or less.
Search and lock targets
1. Radar knob ... OPER
2. Set range with Middle Finger Hat left/right.
3. Set elevation with Middle Finger Hat up/down.
4. When target is within 10 nmi, use TDC to slew cursor and TDC press to lock.
  - Press Dogfight Switch center (Gray Reset Hat press) to unlock.
When target is locked:
  - LOCK light appears on right hand side of radar screen.
  - Radar display changes to boresight view (az/el).
  - Target is the "+" symbol relative to your flight path marker on the radar.
  - B-sweep line on the left becomes range indicator: horiz. line shows target range on vertical axis.

AIM-9 Sidewinders
- AIM-9P-5 - All Aspect
- AIM-9P-3 - Rear Aspect
- GAR-8 (AIM-9B) - Rear Aspect, tailpipe only, non-maneuvering targets
Visual attack
1. Set gunsight MODE knob to MSL.
2. Turn on outer pylon switches to arm missiles. With both armed, left missile will fire first.
3. Set weapon arming switch (guarded) to GUNS MSL & CAMR.
4. Fly to put target in pipper, listen for tone, press and hold Uncage button to allow maneuvering while keeping lock.
5. When you have tone, press and hold Red Button to fire.
  - Don't fire if Excess-G marker appears under pipper.
With radar ranging
Acquire target either manually or automatically:
  - Manually:
    1. Lock target as described in radar section above.
  - Automatically:
    1. Press Dogfight switch forward (Gray Reset Hat forward) to enter Dogfight Missile (DM) mode.
    2. Radar will look for nearest target within 5 nmi and lock it automatically.
2. Radar screen will show steering cues and ranging information, and gunsight pipper will show ranging ring. Gunsight pipper does not point to target, nor does the seeker slave to the radar lock.
3. In-range marker appears at 2:30 o'clock outside pipper. When it appears, target is in range.

Guns
- A/A1 mode - Maneuvering targets?? Or snapshot??
- A/A2 mode - Non-maneuvering or constant-rate targets?? Or tracking shots??
Visual attack
1. Set weapon arming switch (guarded) to GUNS MSL & CAMR.
2. Set gunsight MODE knob to A/A1 or A/A2.
3. Fire with Trigger.
With radar ranging
Acquire target either manually or automatically:
  - Manually:
    1. Lock target as described in radar section above.
  - Automatically:
    1. Press Dogfight switch backward (Gray Reset Hat backward) to enter Dogfight Gun (DG) mode. Pipper same as A/A1 mode??
    2. Radar will look for nearest target within 5 nmi and lock it automatically.
2. Radar screen will show steering cues and ranging information, and gunsight pipper will show ranging ring.
3. In-range marker appears at 2:30 o'clock outside pipper. When it appears, target is in range.

General dogfighting tips:
- Best turn performance at 360 kts.
- Don't go under 300 kts.