052 - A/G - Unguided Bombs, Rockets, AGM-45 Shrike

Master Arm ... ON (B2 button)

Bombs with CMPTR -- Auto release semi-CCIP -- WIP
1. Function Selector knob ... CMPTR
2. Radar knob ... A/G
3. Station switches ... As needed
4. AWRS quantity selector knob ... As needed
5. AWRS drop interval knob ... As needed
6. AWRS mode knob ... SINGLE, RIPPLE, SALVO for either STEP (left half of the dial) or RIPPLE (right half)
  1. CMPTR cannot Ripple Pairs, only Singles.
7. Depress gunsight for easier aiming if needed?? Not sure if this actually works, I think the gunsight may have to be a 0 deg...
8. Dive at target, wings level.
9. Put pipper on target, press and hold Red Button. LABS light below gunsight should illuminate and tone will sound. Keeping wings level, pull up slowly until bombs release. Light and tone should stop, but sometimes they don't.

Bombs with manual bombsight
1. Function Selector knob ... BOMBS & GM ARM
2. Set gunsight depression as needed.

Stores Jettison - WIP
Select pylon to be jettisoned with white emergency jettison selector knob next to emergency jettison handle. Pull handle to jettison that pylon.
DO NOT just pull the emergency jettison handle. Default selection is to jettison all pylons, including A/A missiles.

Bombs - WIP
All
- Intervals	0.06 sec	0.10 sec	0.14 sec
  600 kts	60.8 ft	101.3 ft	141.8 ft
  550 kts	55.7 ft	92.8 ft	130.0 ft
  500 kts	50.6 ft	84.4 ft	118.1 ft
  450 kts	45.6 ft	76.0 ft	106.3 ft
  400 kts	40.5 ft	67.5 ft	94.5 ft
  350 kts	35.4 ft	59.0 ft	82.7 ft
- Calculation: kts / 60 / 60 * 6076.115 / interval = distance
Snakeye
- 80 mils, 200 ft, 500 kts?
- Dropping in ripple can blow up your own plane, possibly due to the bombs hitting each other, or maybe hitting the plane. Interval of 0.14 can help, and making sure you're not pushing anything less than 1 G, but it's not reliably safe with any settings.
Slick
CBU
- Seems to burst after a set amount of time. In level flight, drops at 450 to 500 AGL burst before they hit the ground and give a decent scatter. But in a dive, dropping from that height makes them hit the ground before bursting.
- Scatter is not affected by altitude (bug).

Rockets - WIP
- 10 mils?
- Must be on AWRS OFF and STEP SINGLE (or at least one of those two, not sure if both are needed).
- Fire with trigger.

Guns - WIP
- 10 mils?
- Switches on left console forward, enable gun pod pylons and set to CHARGE.