1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

303 - Flight - Navigation

Points
Type	Prefix & Range	Description
Waypoints/Hazards	W/H01-W/H50	Waypoints or navigation hazards. General flight and navigation points.
Control Measures	C51-C92	Points for depicting friendly and enemy units, airfields, and other graphical control measures for controlling a mission.
Control Measures	C93-C99	Present position reports from other aircraft (not implemented yet).
Target/Threats	T01-T50	Points for targets and threats. May have threat rings.
Target/Threats	T51-T56	Points for storing additional TSD file locations, such as PLT and CPG TRN (Terrain) points. Read-only, cannot be added or edited by the crew.

- Each point has IDENT, FREE, UTM LAT/LONG and ALTITUDE attributes:
  - IDENT -- 2-character alphanumeric identifier, depends on point type. WP=Waypoint, LZ=Landing Zone, BR=Bridge, AE=Enemy Armor, EI=Enemy Infantry, etc., and more, see TSD > POINT > ABR or manual Appendix B.
  - FREE -- Free text, 3-character alphanumeric label. Usually only visible on COORD page, except some types of Control Measures points. Defaults to Wxx, Hxx, Cxx, or Txx (depending on point category) if not specified, where xx is the number of the point.
  - UTM LAT/LONG -- The lat/long of the point in MGRS grid or DD MM.MM.
  - ALTITUDE -- Altitude MSL in ft. Defaults to ground level if not specified.

Add a point
Using cursor:
1. Go to TSD page.
2. POINT OSB (B6), ADD OSB (L2), then select point type with L3-L6 OSB: WP, HZ, CM, or TG.
3. Use Ministick to slew cursor to desired location, press Cursor Enter.
Using KU (Keyboard Unit):
1. Go to TSD page.
2. POINT OSB (B6), ADD OSB (L2), then select point type with L3-L6 OSB: WP, HZ, CM, or TG.
3. IDENT OSB (L1), then on KU:
  1. Enter IDENT (2-character identifier, see manual Appendix B for list) or leave blank, then ENTER.
  2. Enter FREE (3-character label) or leave blank, then ENTER.
  3. Enter UTM LAT/LONG location (defaults to MGRS current location), then ENTER:
    - MGRS format (default): Use left/right arrow keys on KU to move cursor if needed for editing.
    - DD MM.MM format: Press CLR, then enter lat/long as one continuous string with no spaces or decimals, e.g. NddmmmmEdddmmmm.
    - Copy existing point: Press CLR, enter the name of an existing point, e.g. "W01", "T05", etc.
    - Using cursor: Move cursor on map to desired location and press Cursor Enter.
  1. Enter ALTITUDE (ft MSL) or leave blank for ground level at location, then ENTER.

Edit a point
Only FREE, UTM LAT/LONG, and ALTITUDE can be edited.
1. Go to TSD page.
2. POINT OSB (B6), POINT> OSB (L1), enter point type and number on KU ("W01", "T05", etc.) or select point with cursor and Cursor Enter.
3. EDIT OSB (L3), then on KU:
  1. Enter FREE (3-character label) or leave as default, then ENTER.
  2. Enter UTM LAT/LONG location following steps above, then ENTER.
  3. Enter ALTITUDE (ft MSL) or leave blank for ground level at location, then ENTER.

Routes
- Stores up to 10 routes, each with up to 100 points.
- Select routes on TSD page -> RTE -> RTM.
- Routes can be built only with Waypoints/Hazards and Control Measures points, no Targets/Threats.
- Routes usually start with SP (Start Point) and end with RP (Release Point). In practice, they are usually not an exact flight plan but rather a general avenue.
To create route or add/edit points:
1. Go to TSD page -> RTE (B5).
2. ADD OSB (L2), POINT> OSB (L1), enter point type and number on KU?? or select with cursor.
3. END OSB (R5 initially, but will change as you add points??) to insert selected point before end point??
4. Repeat steps 2-3 to add more points, inserting at END or before other points as needed.
To delete points from route:
1. Go to TSD page -> RTE (B5).
2. DEL OSB (L4), select point with R1-R6 OSB or with cursor.