1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - Quick and dirty basic engagement and targeting flow -- WIP

Fence in
1. Master arm ON
2. Ground safety OFF
3. TSD in ATK phase (use OSBs)
4. Laser designator code and Hellfire laser code set (usually to same code)

Human PLT engagement flow with George AI as CPG
1. Press Trim Hat press to bring up George AI menu.
2. Trim Hat left to cycle George's weapons, Trim Hat right to cycle weapon modes. Hellfire LOBL recommended.
3. Press Trim Hat up to tell George to search where you're looking. If targets found, use Trim Hat up/down to go through the list, Trim Hat right to select target, Trim hat left to cancel.
4. Use OSBs on TSD page to set the Acquisition Source to TADS. This will put a crosshair on your HMD where the TADS (and George) is looking.
5. With George in Hellfires mode:
  1. When target is selected, get in range. George's max range is 8000 m, or if you select Hellfires yourself (Gray Reset Hat left), you can go up to 9200 m.
  2. When in range and in constraints, Hellfire box will be large and solid. Command George to fire with Red Button, or manually fire with Trigger if you selected Hellfires.
6. With George in Rockets mode:
  1. Put yourself in rockets mode as well (Gray Reset Hat right), should say COOP on HMD.
  2. George will keep crosshairs on target and lase for ranging, you fly to put crosshair on I-beam reticle. Both crosshair and I-beam follow your HMD visually, but are actually relative to the aircraft centerline.
  3. Center the ball for best accuracy (no sideslip).
  4. Pilot fires rockets with Trigger.
7. With George in Guns mode:
  1. Command George to fire with Red Button. George will fire burst in accordance with burst size setting.
  2. Sometimes he stops lasing the target and won't fire, not sure how to reset...

Human CPG engagement flow with George AI as PLT
1. Optional: Remove the TADS video from the HMD, leaving it only on the TADS display:
  1. Select HMD as Sight (Bottom Hat up), then turn down BRT (brightness) on the TEDAC unit all the way to turn off the background video.
  2. Then select TADS as Sight (Bottom Hat forward), and the brightness on the IHADSS will stay off, while the BRT rocker now controls the TADS image.
2. Press Trim Hat press to bring up George AI menu.
  1. Trim Hat left short to cycle flight mode. Recommended to leave in H-B when hovering.
  2. Trim Hat right short to turn helicopter to where you're looking.
  3. Trim Hat up/down/left/right long to translate slowly while held.
  4. Trim Hat up/down short to change altitude 10 ft at a time.
  5. George will try to hold radar altitude as you go over terrain.
3. Use Joystick and Throttle grip as your primary CPG controls; collective will not be used.
4. Select weapon with Gray Reset Hat; left for Hellfires.
5. Press Bottom Hat forward to select TADS as your Sight. You should now be able to slew the TADS with TDC ministick. TADS controls:
  1. Zoom with Middle Finger Hat: up/down for min/max zoom, and left/right for intermediate zooms.
  2. Change TV/IR with Pinky Wheel forward/back, and press to change IR polarity.
6. To slave your TADS to your helmet sight:
  1. First use OSBs on TSD page to set the Acquisition Source to GHS. You can also set other Acq Sources, like PHS (Pilot's Helmet Sight, to slave TADS to where pilot is looking), or a waypoint/targetpoint (useful if you know exactly where your target is).
  2. Then press Bottom Hat press to toggle slaving. TADS will remain slaved (and TDC won't slew) until you unslave.
7. Lase the target under the crosshairs with Front Thumb Button press and hold. When lasing, diagonal lines appear around crosshair. Max laser range is 9999 m.
8. Ground lock the TADS with Middle Finger Hat press to toggle Linear Motion Compensator. When LMC is on, crosshairs have small bars at the ends, slewing becomes additive/continuous, kind of tricky.
9. When lasing and pointing in the general vicinity of the target, Hellfire box should become large and solid, meaning Hellfire sees the laser and is OK to fire.
10. Press Trigger to fire. Keep lasing until impact. Fire another around 8-10 seconds apart; after first missile hits, keep lasing the whole time while slewing to the next target so it sees the laser spot move.