1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

506 - A/G - 30 mm Cannon, Rockets

Fence In:
- Master Arm ... ARM
- TSD ... ATK phase
- Laser ... Armed (WPN page -> CHAN -> UTIL -> LASER)

M230 Chain Gun -- 30 mm cannon with 1200 rounds, or 300 rounds if aux fuel tank (Robbie tank) is installed
1. Gray Reset Hat back to select gun.
2. Gun mode ... NORM for normal aiming that follows the sight, or FXD for fixed forward.
PLT or CPG with HMD:
1. Select HMD as sight (Coll. Middle Hat up).
2. Set range to auto: WPN page -> MANRNG -> type "A" on the KU and press ENTER.
3. Look at target and fire with Trigger.
CPG with TADS:
1. Set acquisition source, slave (Bottom Hat press) TADS to target, then de-slave.
2. Lase target with Front Thumb Button press and hold.
3. Fire with Trigger.

Hydra 70 Rockets -- 70 mm rockets, M261 launcher
Due to possible engine surge from exhaust smoke, it is preferred to load rockets on the outboard pylons.
Using COOP mode with TADS (direct fire)
1. PLT - Sight select ... HMD (Coll. Middle Hat up)
2. CPG - Sight select ... TADS (Coll. Middle Hat right or Thr. Bottom Hat forward)
3. CPG - Set Acquisition Source (TSD page -> ACQ OSB??) and acquire target:
  - If target is acquired visually, select PHS or GHS.
  - If target is at a point in the aircraft database, set point as Acquisition Source with COORD page or using the cursor on the TSD page.
1. CPG - Press SLAVE button (Bottom Hat press) to slew TADS to target, then SLAVE again to deslave and go back to manual tracking.
2. PLT - Select Rockets with Gray Reset Hat right.
3. CPG - Select Rockets with Gray Reset Hat right.
  - HAD (High Action Display at bottom of HUD) should show COOP.
  - (NOTE: You must select rockets on TADS grip, not cyclic, to enable COOP mode; the mapping takes care of this.)
1. On WPN page, select and setup rockets.
2. CPG - Range target using Laser, Nav, Auto, or Manual as needed.
3. CPG - Call "Match and Shoot" to instruct pilot to align the Rocket Steering Cursor as needed and fire.
4. PLT - Match and Shoot:
  1. Adjust for "aerodynamic" trim (centered ball).
  2. Rocket Steering Cursor (I-beam) is relative to your HMD LOS cross (aircraft centerline).
  3. Maneuver to align the I-beam on your HMD LOS cross.
  4. When aligned, fire with Trigger.

Rocket zones
- Rocket pods have 5 zones: A, B, C, D, and E
- Different rockets can be loaded in each zone, and zones can be selected on WPN page.
- Zone A ... 24 total: Outboard rocket pods, outer ring of 12 rockets.
- Zone B ... 8 total: Outboard rocket pods, top and bottom 2 rockets of the inner 6.
- Zone C ... 24 total: Inboard rocket pods, outer ring of 12 rockets.
- Zone D ... 8 total: Inboard rocket pods, top and bottom 2 rockets of the inner 6.
- Zone E ... 12 total: All rocket pods, inner middle line of 3 rockets.