1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

507a - A/G - AGM-114K Hellfire self-designating

Fence In:
- Master Arm ... ARM
- TSD ... ATK phase
- Laser ... Armed (CPG WPN page -> CHAN -> UTIL -> LASER)

Tested ranges from 50 ft AGL hover -- Min laser range is 500 m, max is 9.999 km
Mode	Traj	Min	Max
LOAL	HI	3.8 km	9.4 km
LOAL	LO	3.8 km	9.3 km
LOAL	DIR	??	??
LOBL	n/a	750 m	9.3 km

AGM-114K Hellfire II semi-active laser, self-designating -- WIP
Laser Hellfire trajectories -- There are 4 trajectories: LOBL, LOAL DIR, LOAL LO, and LOAL HI. If the missile sees the laser designation at the time of launch, it will always use LOBL, otherwise it will use LOAL DIR/LO/HI. In LOAL, selecting DIR will set the missile constraints relative to the Sight LOS (TADS or HMD), while selecting LO or HI will set the missile constraints relative to the ACQ Source (which could be the TADS, or a waypoint).
1. Set up options on WPN page (WPN OSB):
  1. CHAN sub-page (T1 OSB) sets the laser channel the missiles will look for
    1. Select CHANNEL number at top (B2-B4 OSBs)
    2. Then select code A-R to be set to that channel with appropriate OSB.
  2. CODE sub-page (T4 OSB):
    - Sets code for TADS laser designator, toggle which to set with T2 OSB.
  1. TYPE (R1 OSB) ... SAL for semiactive-laser-guided Hellfires
  2. MODE (R2 OSB) ... NORM for normal missile sequencing
    - RIPL is for Ripple Fire (alternating missiles with wingman), MAN is for manual using missile step button
  1. TRAJ (R3 OSB):
    - HI -- Steep climb immediately after launch to clear close obstacles, slaves seeker to ACQ point
    - LO -- Shallow climb, slaves seeker to ACQ point
    - DIR -- Direct trajectory, slaves seeker to TADS LOS
  1. LRFD (R5 OSB)
    - FIRST ... Selects first laser rangefinder reflection for ranging.
    - LAST ... Selects last laser rangefinder reflection for ranging.
  1. PRI (R1 OSB) ... As desired, this is the main missile laser code
  2. ALT (R2 OSB) ... Not needed, only used for Ripple Fire
  3. SAL SEL ... SAL 2 for AGM-114K and later (SAL 1 and AUTO are for AGM-114F and earlier)
2. LOBL:
  1. Designate target with TADS and begin lasing (diagonal lines appear in the TADS crosshairs).
  2. When you're pointed within the missile constraints box and the missile is tracking the laser, the constraints box will be large and solid.
  3. Press Trigger to fire.
3. LOAL:
  1. Set ACQ (Acquisition Source) to target waypoint.
    - Create a target waypoint with TADS by pressing STO button (Ministick press).
  1. When you're pointed within the missile constraints box, the constraints box will be small and solid.
  2. Press Trigger to fire.
  3. When remaining TOF (Time of Flight) is around 12 seconds, begin lasing the target.
2. Rapid fire:
  1. Launch missiles about 8 seconds apart. HAD will show FIRE MSLS briefly at 8 seconds after launch as a cue.
  2. When 1st missile has 12 seconds remaining TOF, HAD will show LASE 1 TGT. Begin lasing.
  3. As each missile impacts, HAD will show LASE 2 TGT, LASE 3 TGT, etc.
3. Ripple fire:
  1. This alternates missiles between the PRI and ALT laser channels (WPN > CHAN, and shown at the bottom of the main WPN page)
  2. Your CODE (TADS laser code) should be set to the PRI channel, your wingman's set to the ALT channel.
  3. Both aircraft designate targets, you are the shooter, each shot alternates between guiding on your laser or your wingman's.