1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

601 - Notes, Quirks, and Trivia

General DCS helicopter combat
- Stay under 15 m (50 ft), preferably under 10 m (33 ft), to avoid all SAMs.
- Don't get closer than about 4.5 km to anything with guided missiles (e.g. tanks, APCs, IFVs).
- Don't get closer than about 2.5 km to anything with a significant AAA gun (e.g. Shilka, Gepard, M163, etc.)

Apache-specific
- General crew responsibilites:
  - CPG:
    - Designate and fire Hellfire missiles.
    - Designate targets for rockets, while PLT aims and fires.
    - Searching and acquiring, identifying, lasing, and storing targets or points of interest.
    - Update aircraft navigation and routing or direct-to point.
    - Tune radio frequencies.
    - Communication with other units and coordination with other CPGs on targets and areas of fire.
  - PLT:
    - Aim and fire rockets, while CPG designates targets.
    - Aim and fire gun.
    - Fly to best position the CPG for using the sensors and weapons.
    - Maintain SA and tactical situation, maneuver as needed to keep sensors and weapons in limits.
    - Watch and secure immediate surroundings, use gun for pop-up threats.
- 2-ship flights, the basic unit:
  - Distance between aircraft may be as little as 2-5 rotor discs or as much as a kilometer or more.
  - Aircraft should be close enough to be mutually supporting.
  - "Combat Cruise" formation is echelon, with enough room to allow Lead to maneuver freely.
  - "Combat Spread" formation is line-abreast.
- Terrain flight modes:
  - NOE (Nap Of the Earth) -- Less than 25 ft above highest obstacle. Use Bounding Overwatch, don't go further than your suppression weapon (usually the gun) can cover.
  - Contour -- 25 to 80 ft above highest obstacle. Use Traveling Overwatch and Combat Cruise formation.
  - Low-level -- 80 to 200 ft above highest obstacle, usually level high-speed flight.
- Trimming modes:
  - Use "nose-to-tail" trim (velocity vector in line with aircraft centerline) for NOE flying. This keeps your profile as narrow as possible, reducing risk of tree strikes. Also used for landing at touchdown.
  - Use "aerodynamic" trim (centered ball) for rocket attacks for better accuracy (so the rockets don't have a crosswind coming out of the tubes), and landing approach.
- The KU (Keyboard Unit) can be used as a calculator with *, /, +, and - buttons, and = (ENTER).
- "It should also be noted that if the CPG uses the TEDAC LHG WAS, only the CPG’s TEDAC LHG trigger will be active; accordingly, if the CPG uses the cyclic WAS, only the CPG’s cyclic trigger will be active."
  - Needs verification...
- Exclusive controls:
  - Back seat:
    - External lighting.
    - CMWS.
    - Engine and APU start switches.
    - Rotor brake.
    - Battery switch.
    - Parking brake.
    - Rear/middle windshield wiper controls.
    - Free (outside) air temperature backup (thermometer on left cockpit wall) (Free Air Temperature can be seen on any MFD in the A/C -> UTIL page)
    - Backup flight instruments (SAI, airspeed, altitude)
  - Front seat:
    - TADS display and associated controls.
    - Front windshield wiper controls.
    - Display processor selector switch (not used in game).