302 - Flight - Radios, Countermeasures, Jettison, Radio Navigation

Radio setup and tuning
COM1	ARC-186(V)	VHF	Rec: 108.000 to 115.975 / T/R: 116.000 to 151.975 MHz	AM	Primary radio
COM2	ARC-164(V) (HAVE QUICK)	UHF	T/R: 225.000 to 399.975 MHz	AM
COM3	ARC-201D (SINCGARS)	LVHF	T/R: 30.000 to 87.975 MHz	FM	2x, FM1 and FM2
COM4	ARC-220	HF	T/R: 2.000 to 29.999 MHz	FM

Preset frequencies using EUFD:
EUFD cannot tune IDM or SINCGARS channels.
1. Press P button to show preset channel list.
2. Use RTS rocker to select radio to set.
3. Use WCA rocker to select preset channel from list.
4. Press ↵ (Enter) to tune selected radio to preset.
5. Press 🗘 (Swap) to switch primary and secondary frequencies for selected radio.
EUFD symbols:
◀ ▪	You have selected this radio for voice transmission.
▪ ▶	The other crewmember has selected this radio for voice transmission.
◀ ▶	Both crewmembers have selected this radio for voice transmission.
▪ ▪	Neither crewmember has selected this radio for voice transmission.
⛋	You have selected this radio for IDM transmission.
◆	The other crewmember has selected this radio for IDM transmission.
◼	Both crewmembers have selected this radio for IDM transmission.
*	Squelch on.
Manual frequencies on COM page (COM OSB):
When radio is tuned to a manual frequency, IDM cannot be used on that radio.
1. Press COM OSB to go to COM page.
2. Press MAN OSB to go to MAN sub-page.
3. Press L1-L4 OSB to select VHF, UHF, FM1, or FM2 radios. Press R1 or R3 to select HF Receive or HF Transmit frequencies respectively.
4. Enter frequency on KU (Keyboard Unit) and press ENTER to set.

Countermeasures setup
1. On CMWS control panel (PLT front right canopy frame):
  1. Power knob ... ON
  2. AUDIO and LAMP knobs ... As desired
  3. ARM/SAFE switch ... ARM
  4. CMWS/NAV switch ... CMWS (sets audio to CMWS; NAV is ADF receiver audio)
    - Because the CMWS is a post-production mod, it uses the ADF audio channel, hence the switch.
  1. BYPASS/AUTO switch ... BYPASS??
2. Screen shows remaining Flares and Chaff, arrows show direction to threat, D=Dispensing, R=Ready.

Jettison
1. Stores Jettison Panel is on left console (both crew stations).
2. Press ARM buttons for stations you want to jettison, then press JETT button.
3. Or, use the Emergency Jettison switch on the collective to jettison all external stores.

Navigate to a beacon (NDB) with ADF (AN/ARN-149)
1. Press TSD OSB to go to TSD page.
2. Press INST OSB (L1) to go to INST sub-page.
3. Press UTIL OSB (T6) to go to UTIL sub-page.
4. Press ADF OSB (B6) to toggle ADF power on.
5. Select ADF frequency:
  1. Preset: Press L2-L6 or R2-R6 OSBs.
  2. Edit a preset:
    1. Select preset to edit.
    2. Press ID> OSB (B4), enter Morse identifier on KU and press ENTER.
    3. Press FREQ> OSB (B5), enter frequency on KU and press ENTER.
  3. Manual tuning:
    1. Press INST OSB (L1)?? to return to INST sub-page.
    2. Press FREQ> OSB (L3), enter frequency on KU and press ENTER.
    3. Press LAST FREQ OSB (L5) to toggle back and forth between current and previous frequency, useful when navigating to intersection??
6. Set ADF audio if needed on CMWS control panel switch (PLT front right canopy frame)