502 - A/G - 30 mm Cannon, Rockets

Fence In:
Master Arm ... ARM

M230 Chain Gun -- 30 mm cannon with 1200 rounds
TODO

Hydra 70 Rockets -- 70 mm rockets, M261 launcher
Due to possible engine surge from exhaust smoke, rockets should preferentially be loaded on the outboard pylons.
Using COOP mode with TADS (direct fire)
1. PLT - Sight select ... HMD
2. CPG - Sight select ... TADS
3. CPG - Set Aquisition Source and acquire target
  - If target is acquired visually, select PHS or GHS.
  - If target is at a point in the aircraft database, set point as Acquisition Source with COORD page or using the cursor on the TSD page.
1. CPG - Press SLAVE button to slew TADS to target, then SLAVE again to switch to manual tracking.
2. PLT+CPG - Select Rockets with Gray Reset Hat right.
  - HAD (High Action Display at bottom of HUD) should show COOP.
1. On WPN page, select and setup rockets.
2. CPG - Range target using Laser, Nav, Auto, or Manual as needed.
3. CPG - Call "Match and Shoot" to instruct pilot to align the Rocket Steering Cursor as needed and fire.
4. PLT - Match and Shoot:
  1. Trim for aerodynamic (centered ball).
  2. Turn toward Rocket Steering Cursor.
  3. ...TODO