503 - A/G - AGM-114 Hellfire

Autonomous (self) lasing, AGM-114K Hellfire II semi-active laser -- WIP
LOBL and LOAL -- The only difference is whether the missile sees the laser designation at the time of launch. If it does, then it's LOBL, if not, then it's LOAL. LOAL has tighter launch constraints.
1. Set up options on WPN page (WPN OSB):
  1. CHAN sub-page (T1 OSB) sets the laser channel the missiles will follow
    1. Select CHANNEL number at top (B2-B4 OSBs)
    2. Then select code A-R to be set to that channel with appropriate OSB.
  2. CODE sub-page (T4 OSB):
    - Sets code for laser designator, toggle which to set with T2 OSB.
  1. TYPE (R1 OSB) ... SAL
  2. MODE (R2 OSB) ... NORM for normal missile sequencing
    - RIPL is for Ripple Fire (not implemented yet)
  1. TRAJ (R3 OSB):
    - HI -- Steep climb immediately after launch to clear close obstacles
    - LO -- Shallow climb
    - DIR -- Direct trajectory
    Any trajectory can be used for either LOBL or LOAL, but DIR is mostly used for LOBL, and LO and HI are mostly used for LOAL.
  1. LRFD (R5 OSB)
    - FIRST ... Selects first laser rangefinder reflection for ranging.
    - LAST ... Selects last laser rangefinder reflection for ranging.
  1. PRI (R1 OSB) ... As desired, this is the main missile laser code
  2. ALT (R2 OSB) ... Not needed, only used for Ripple Fire (not implemented)
  3. SAL SEL ... SAL 2 for AGM-114K and later (SAL 1 and AUTO are for AGM-114F and earlier)
2. LOBL:
  1. Designate target with TADS and begin lasing (diagonal lines appear in the crosshairs).
  2. When you're pointed within the missile constraints box and the missile is tracking the laser, the constraints box will become large and solid.
  3. Press Red Button to fire??
3. LOAL:
  1. Designate target with TADS, or on TSD page with COORD OSB or cursor.
  2. When you're pointed within the missile constraints box and the missile is tracking the laser, the constraints box will become large and solid.
  3. Press Red Button to fire??
  4. When remaining TOF (Time of Flight) is around 12 seconds, begin lasing the target.
4. Rapid fire:
  1. Launch missiles about 8 seconds apart. HAD will show FIRE MSLS briefly at 8 seconds after launch as a cue.
  2. When 1st missile has 12 seconds remaining TOF, HAD will show LASE 1 TGT. Begin lasing.
  3. As each missile impacts, HAD will show LASE 2 TGT, LASE 3 TGT, etc.

Remote lasing -- WIP
Same as Autonomous lasing above, but set the missile code to the buddy lase frequency.

Ripple firing with FCR (not implemented yet)
TODO

Priority Fire Zone (PFZ) and wingman engagement (not implemented yet?)
TODO