108 - Controls - TADS - Joystick
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Trigger
- P1: Fire weapon if in constraints
- P2: Fire weapon overriding constraints
Flip-down trigger
- P: Trimmer button (hold for 3 seconds to allow SAS to fully desaturate)
- S-P: Trimmer reset
Red button
- P: --
- S-P (3x): --
Upper gray button
P: Center VR view
Lower gray button
P: Sight Slave button (RHG)
Trim hat -- Force Trim/Hold Mode switch
- U: Trimmer button (hold for 3 seconds to allow SAS to fully desaturate)
- D: Disengage all hold modes
- R: Altitude hold
  - To engage, vertical velocity must be less than 200 fpm at hover, less than 400 fpm at cruise. Holds radar altitude when 0-40 kts and 0-1428 ft AGL, baro altitude otherwise.
- L: Attitude hold
  - If below 5 kts, will hold ground position; if between 5-40 kts, holds constant velocity.
- P: Toggle George AI menu
- U/D/L/R: George AI menu controls (when George AI menu is active)
Dish hat -- Symbology Select Switch
- U: Bob up
- D: Hover
- L: Cruise
- R: Transition
- P: Display FLT page
MANVR/PC hat -- Mouse and zoom
Index Finger Hat -- View and Game controls
- F: F6 Weapon view	S-F: Active pause
- B: F2 External view	S-B: Info bar view toggle
- U: F1 Cockpit view	S-U: Rearm/Refuel window
- D: F10 Map view	S-D: Show controls indicator
- P: Toggle show control stick	S-P: Toggle show pilot body
Gray Reset hat -- Weapon Action Switch
- P: Trimmer button (hold for 3 seconds to allow SAS to fully desaturate)
- S-P: Trimmer reset
- L: Select Hellfire missile
- B: Select 30mm cannon
- R: Select rockets
Brake lever
- Axis: --
- P: --