201 - Cold Start

Cold Start -- TODO
1. MSTR IGN switch ... BATT (or EXT if using external power, set to BATT after APU is started)
  1. Must start APU within 1 minute if temp > 43 deg C/109 deg F, 3 mins if temp between 32-43 deg C, 20 mins if temp < 32 deg C.
2. Lights ... As needed
3. APU push button ... Press to start APU
4. DMS page -> DTC ... MASTER LOAD OSB (not implemented yet)
5. TODO
6. Battery and APU
7. Start engines
8. Turn on avionics and MFDs
9. Turn on and boresight sighting systems
10. ...

Proceed with remaining takeoff checklist on next page.

From -10 manual:
1. Canopy ... Close
2. Parking Brake ... Set
3. RTR BRK switch ... Off (left console forward outboard, under power levers))
4. DTC ... Installed (data card)
5. MSTR IGN switch ... BATT (or EXT if using external power, set to BATT after APU is started)
  - Must start APU within 1 minute if temp > 43 deg C/109 deg F, 3 mins if temp between 32-43 deg C, 20 mins if temp < 32 deg C.
1. Lights ... As needed
2. APU push button ... Press to start APU
3. KU, MPD, UFD/EUFD knobs ... On, and brightness as desired
4. Cockpit heat and A/C ... As desired
5. DTC ... Select Load
6. EGI (Embedded GPS/INS) ... Verify keys??
7. IHADSS boresight ... perform
8. TADS boresight ... perform (if CP/G)
9. Standby attitude indicator ... Uncage
10. On MFD, go to ENG page
11. If BUCS (backup control system) is engaged, do not start engines until clearing. BUCS can become engaged if external power is applied to aircraft without hydraulic power. To clear BUCS:
  1. RTR BRK switch ... BRK
  2. POWER levers ... OFF
  3. DMS IBIT page ... Selector
  4. ACFT/COM-FLT CNTRLS-PRFLT ... Select, follow IBIT instructions until test is complete
  5. RTR BRK switch ... OFF
12. TSD and FLT pages ... Select
13. INS align -- TODO
14. Start first engine (either engine can be started first):
  1. Cold engine (4 hours since last shutdown):
    1. ENG START switch ... START (left console outboard)
    2. When NG starts going up, POWER lever ... IDLE
  2. Warm engine
    1. START switch ... IGN OVRD
    2. Allow NG to increase to 18-20%, then START switch ... OFF
    3. When NG is back below 5%, START switch ... START
    4. POWER lever ... IDLE
15. Start second engine:
  1. Follow steps above for conventional startup.
  2. For cross-engine start:
    1. ENG page ... Select
    2. Increase collective to 95% NG on the other engine.
    3. Follow steps above for cold or warm engine start.
    4. Collective ... reduce to flat pitch
16. POWER levers ... Advance smoothly to FLY
17. APU ... OFF
18. Parking Brake ... Release