301 - Ground - Preflight, Performance Limits

PILOT Before takeoff (hot start or auto cold started) -- TODO
1. RWR
2. IFF
3. Lights (left console rear)
  - SIGNAL knob controls warning/caution/advisory (WCA) lights. If FLOOD knob is turned up past midpoint, WCA lights will automatically be set to daytime brightness. To restore nighttime brightness, ensure FLOOD knob is set lower than halfway, then turn SIGNAL knob to RST position and then back down to desired nighttime brightness.
Radios
  - Volume and squelch controls are on right console forward.
1. Weapon switches
2. HMD
3. Navigation system
4. Engine dust protection and de-icing systems
  1. Engine anti-ice should be activated if air temp is less than 41 deg F/5 deg C.
5. Crew station heat and A/C
6. Tail wheel ... Unlock
7. Parking Brake ... Release
8. POWER levers ... FLY

GUNNER Before takeoff, for human gunner only -- TODO
1. TADS
2. ...

Performance limits
- Max fully loaded speed: ~310 kph (167 kts) (with 4x ATGM + 4x rocket pods or 8x ATGM + 2x rocket pods)
- Vne speed: 197 kts, or less depending on density altitude and temperature. Shown on PERF page. Retreating blade stall happens ~370 kph, may roll uncontrollably to the right; flatten collective immediately to attempt recovery.
- Speeds:
  - With symmetrical external tanks: 130 kts
  - Stores jettison: 130 kts (minimize side slip)
  - External tank jettison: 100 kts
  - Sideways/backwards flight: 45 kts
  - Searchlight:
    - Moving light: 90 kts
    - Not moving: 200 kts
- NR (rotor RPM) limits:
  - Max: 110%
  - Transient: 106-110% (high rotor warning light at 106+%)
  - Normal: 95-105%
  - Transient: 0-94%
- T700-GE-701C engine TGT limits:
  - Max: 949 °C
  - Single engine transient: 897-949 °C, 12 sec
  - Single engine contingency: 879-896 °C, 2.5 min
  - Intermediate rated power: 871-878 °C, 10 min
  - Maximum during start: 851 °C
  - Intermediate rated power: 811-870 °C, 30 min
  - Max continuous: 810 °C
  - Normal: 0-810 °C
- Torque limits:
  - Max: 115%
  - Transient: 101-115% (6 sec)
  - Normal: 0-100%