301 - Flight - Taxi, Takeoff, Landing

Ground Taxi
1. Collective to 27-30% TQ or as required for conditions.
2. Maintain 5-6 kts or as appropriate for conditions.
3. Unlock tailwheel before turning, re-lock when straightened out.

Takeoff
1. Check hover power on PERF page -> PERF, HOVER Q values.
  1. IGE and OGE columns give required torque for hovering with current weight and temperature.
2. Light-on-wheels should be about 80% of HOVER Q REQUIRED IGE value.
3. Perform Hover Power Check if needed:
  1. Get light-on-wheels and trim, then increase power for 5-foot hover and trim.
  2. Check HOVER Q values to make sure INDICATED (your current power) matches REQUIRED IGE and is lower than GO-NO/GO OGE.
  3. If INDICATED is not lower than GO-NO/GO OGE, reduce weight, 200 lbs per 1% torque reduction, until you will be able to hover OGE.

Landing
1. Articulating pylons ... GROUND STOW (in WPN UTIL page)
2. After landing, POWER levers ... IDLE
3. Allow engines to idle for 2 minutes before shutting down. If engine is shut down before cooling for 2 minutes at idle, it should be restarted within 5 minutes, or wait 4 hours for complete cooldown before restarting.
4. When below 50% NR, RTR BRK switch ... BRK
5. Cage SAI, Lights off, Stabilator to zero, MSTR IGN ... OFF