201 - Ground - Cold Start

Cold Start -- (manual startup is much faster than auto)
1. Master Mode knob ... BER (standby)
2. HUVUDSTRÖM (Main Electric Power) switch ... TILL (on) (left console front outboard)
3. HUVUDWARNING button ... Press to cancel Master Caution (instrument panel left top)
4. LT-KRAN (Low-pressure Fuel Valve) switch ... TILL (on) (left console front outboard)
5. GENERATOR switch ... TILL (on) (left console front outboard)
6. High Pressure Fuel Valve ... Open (sets throttle to idle) (pinky lever on outboard of throttle, Bottom Thumb Button to toggle)
7. Start System switch ... T (left console in front of throttle)
  - Engine should stabilize around 55% to 65% N2 RPM ("Varv" gauge on right instrument panel).
  - Switch should return to F (Off) after engine reaches idle.
1. Canopy ... Close (T7 switch down and hold)
2. Ejection Seat ... Arm (above and right of head)
  - HUV O STOL master caution light should go out when canopy is closed and seat is armed.
1. Oxygen switch ... TILL (on) (right console forward outboard)
2. Pitch trim ... 3 deg nose up ("Nos Upp") (gauge on left console far forward outboard)
3. If in icing conditions: AVISN MOTOR switch ... TILL (right side under canopy rail)
4. Altimeter ... zeroed
5. Backup altimeter ... zeroed
6. Magnetic Declination ... Open cover (right console) and set to: (not working??)
  - +6.4 deg for Caucasus
  - +14.2 deg for Nevada
  - +1.3 deg for Persian Gulf
  - -5.0 deg for Normandy
  - +0.2 deg for English Channel
  - +5.2 deg for Syria
1. After engine is started, Master Mode knob ... NAV, then wait 2 minutes before throttle up
2. Parking Brake ... Release (tap brakes or release handle in center console between legs)

Proceed with pre-flight checklist on next page.