505 - A/G - RB 04E antiship missiles (older missiles)

Before any attack
1. Weapon Selector dial to ATTACK, Release Mode switch as needed. If SERIE is used, missiles will automatically separate after launch.
2. Set QFE on altimeter to QNE (sea level pressure).
3. Height 50 m to 425 m.
4. Range 24 km (13.0 nmi) max, 12 km (6.5 nmi) min
5. Missile's radar range 8 km (4.3 nmi), FOV +/-28 deg.

Quick attack in NAV mode using default missile behavior
1. Set Master Mode dial to NAV.
2. Targeting Mode switch to ENKEL (single target) or GRUPP (targets in group within 2.7 km and in line parallel to missile travel)
1. Point plane at ships (either visually or using radar).
2. (Optional) Set target waypoint at ships, set Master Mode dial to ANF. Ranging cues will appear on radar screen.
3. Press and hold trigger until missile fires. Missiles will immedately drop to 10 m ASL and fly in a straight line until they find targets with their radar, and attack the first one (or group) they see.

Planned attack using mark points (BXn)
Place BXn markers using F10 map, or in flight using the Radar nav fix/update method (see Nav Fix checklist for steps):
  1. Set Master Mode dial to NAV.
  2. Turn radar on to A1 setting (PPI display) and set range as needed.
  3. Update/set BX8 first. The computer then automatically creates BX6 and BX7. You need to set BX8 first because updating its location also moves BX6 and BX7.
  4. Then update BX6 (descent point) and BX7 (dog leg) manually.
1. Set Master Mode dial to ANF.
2. Set Targeting Mode switch as needed. Use VALB (default) to customize missile behavior (see below). Use STD to keep default missile behavior.
3. Make sure you have not passed BX6, or the missiles will not fire.
4. HUD symbology will show range bars at the bottom. When horizontal line is between the two vertical lines (in range), press and hold trigger until missile fires.

Missile behavior can be customized (see manual for full explanations)
- It can lock onto the first target it sees, or randomly select a target in an area.
- It can be set to sea-skim on approach or fly at 30 m altitude.
- It can be set to search larger or smaller areas around the target point (BX8).
- It can be set to have left and right boundaries to the search area.
- It can be set to sea-skim to impact, or fly at 10 m on the terminal approach.
- Default behavior is to lock onto the first target it sees (quick attack) or the target closest to BX8 (planned attack), sea-skim the entire time including terminal, and search a large area.

TAKT - IN presets (use with Targeting Mode switch set to VALB)
- 800000 - (default) Single target closest to BX8, large search area.
- 800001 - Random target from the three closest to BX8, medium search area.
- 800002 - Random target from all targets around BX8, medium search area.
- 800003 - Random target in a group of ships (within 3 km of each other) closest to BX8, large search area.
- 800004 - Single target closest to missile heading, search anywhere along heading, not just near BX8. (Similar to Quick attack?)
- Press LS to save the value after entering.

Mark point (BXn) types
- BX6 = Descent point, where missile will descend from launch altitude.
- BX7 = Course change point.
- BX8 = Assumed Target Position (ATP) aka the target point.
- BX9 = (optional) Self-destruct point, should be at least 5 nmi from BX8, more is OK. If no target is found at BX8, missile will turn and self-destruct at BX9.
- Sum of course changes must be < 135°.