506 - A/G - RB 05 MCLOS missile

Before attack:
1. Set Weapon Selector dial depending on attack profile:
  1. MARK DYK for ground targets, detonates on impact.
  2. SJO PLAN for naval targets, detonates after short delay.
  3. LUFT RR for air targets, detonates when within 6 m of target.
2. Missile range approx 10 km, battery life is 40 seconds from Trigger Unsafe.

On attack run toward target waypoint:
1. Set Master Mode dial to ANF.
2. When 10 away, set Trigger Unsafe (hold Trigger 1st stage, or press Flip-down trigger).
  - IMPORTANT: Missile battery lasts only 40 seconds starting when Trigger Unsafe is pressed.
1. Press Trigger 2nd stage to fire.
2. Guide missile visually with RB 05 stick pitch up/down/left/right (Dish Hat up/down/left/right, or Dish Hat press and hold to make main flight stick steer the missile)