041 - Takeoff, landing, and general flight

Before Takeoff
1. Set up map waypoint markers. See below for marker types.
2. Use kneeboard to check data cartridge source. LCtrl-LAlt-C to increment source, LCtrl-LShift-C to decrement.
3. With data cartridge inserted, set REF LOLA - IN, enter 9099, press LS.
4. When display shows zeros again, set AKT POS - OUT.
5. Do a sanity check on the waypoints. Make sure you have a target (Mn) waypoint. If not, see below on how to change a waypoint to a different type.
6. Set QFE on altimeter to value shown in kneeboard for target waypoint.
7. Set SLAV SI switch to F (turns off HUD declutter at low altitude).
8. Weapon Selector dial and Interval dial as needed.
9. Set Master Mode dial to NAV (default).

Takeoff
1. Rotate at 250 kph with full AB, 280 kph with Mil power.
2. Put Velocity Vector level with the tallest of the three vertical lines to avoid tail strike.

Landing
1. Set QFE on altimeter to value shown in kneeboard for landing waypoint.
2. Set AKT POS - OUT, press L-MAL waypoint button to select landing waypoint.
3. Set Master Mode dial to LANDNING P/O (for visual approach).
4. Arm thrust reverser (lever in cockpit will pull out).
5. Gear down under 600 kph.
6. Minimum speed 260 kph.
7. Put velocity vector on HUD line under the horizon line to get 12 degrees AOA and 3 degree glide slope.
8. Can use autothrottle (throttle Bottom Thumb Button) to maintain 12 deg AOA.
9. When front wheel touches down, thrust reverser will engage. Use full throttle to slow down quickly (afterburner will not light).
10. Reduce throttle before coming to a complete stop and use brakes for final stop.
11. DO NOT USE BRAKES WHILE MOVING BACKWARDS.

Map waypoint marker types
- Bn	Nav waypoints.
- Mn	Target waypoints.
B and M numbers should be sequential (1-9) through all the B and M markers.
- Un	Popup point (optional). The n is the number of the waypoint that the popup point is for.
- BXn	Reference point. The n is independent of the Bn/Mn numbers. BX6-9 are used for RB 15 antiship missiles.
- LS	Starting position (your current position will be used automatically when loading the cartridge, no need to make a F10 marker for this).
- L1	Landing waypoint (defaults to same as LS).
- L2	Alternate landing waypoint (optional).
e.g. Typical flight plan might be LS -> B1 -> B2 -> M3 (with optional U3 popup point) -> M4 -> B5 (optional -> L1 (with optional L2 alternate landing))

To change a nav waypoint (Bn) into a target waypoint (Mn) or vice versa
1. Set TAKT - IN.
2. Enter 9 (Or to change target waypoint to nav waypoint, enter 0), then press the button of the waypoint you want to change.
3. Set AKT POS - OUT.

Autothrottle (AFK) -- Lever next to landing gear, behind left elbow (throttle Bottom Thumb Button)
- Gear up: AFK maintains speed of 550 kph.
- Gear down: AFK maintains 12 deg AOA for landing.