042 - Nav Fixes and Updates

Notes
- Updating a Bn navigation waypoint will update all the other waypoints, including target waypoints.
- Updating a Mn target waypoint will update only that waypoint.
- Updating the BX8 marker waypoint will update BX6, BX7, and BX9 as well, but updating BX6, BX7, or BX9 will only update that specific waypoint.

Visual fly-over fix
1. Radar must be Off.
2. Destination Indicator should show the waypoint you want to correct, and that you're going to fly over the actual location of.
3. Press T1 detent on radar stick. Destination Indicator should show a solid E.
4. When you are directly over the actual location of the waypoint, press the TV detent on radar stick.
5. Waypoint location will be updated and next waypoint will be selected.

Radar fix
1. Radar must be On in A1 mode (PPI display).
2. Destination Indicator should show the waypoint you want to correct, and that you're going to select the exact location of on the radar.
3. Current location of waypoint will show as a circle on the radar screen.
4. Press T1 detent on radar stick. Destination Indicator should show a flashing E, and a cross will appear on the radar screen.
5. Use the radar control stick (ministick on throttle) to move the cross on the radar screen to the waypoint's correct location.
6. Press the TV detent on radar stick.
7. Waypoint location will be updated.