061 - M/71 bombs and BK 90 glide cluster bombs

M/71 bombs (high drag)
1. Weapon Selector dial to SJO PLAN (default), Interval dial as needed (distance in m), Release Mode switch to SERIE (default).
2. Set Master Mode dial to NAV.
3. Set QFE on altimeter to value shown in kneeboard for target waypoint.
4. Hold trigger UNSAFE to show HUD symbology.
5. Bombs will fall between dot and circle.
6. Speed 0.7 to 0.9 Mach. Use Stage 2 AB for about 0.85 Mach.
7. Height 50 m to 200 m.
8. Hold trigger down until all bombs are gone.

ARAK M/70B rockets
1. Weapon Selector dial to ATTACK, Release Mode switch to SERIE (default).
2. Second Release Mode switch switch to ENKEL (down) for single rocket per pod per trigger press, GRUPP for all rockets per pod.
3. Set Master Mode dial to ANF.
4. Set QFE on altimeter to value shown in kneeboard for target waypoint.
5. Fly to put center dot into the target indicator ring.
6. Hold Trigger Unsafe to begin radar ranging. Target indicator ring will disappear.
7. Distance line at bottom flashes when within 2 seconds of release.
8. When in range, "wings" appear to either side of center dot. Press and hold trigger to fire.

BK 90 Mjolnir glide cluster bomb -- MJ1 is 72x HE/frag bomblets, MJ2 is 24x AP bomblets
1. Weapon Selector dial to ATTACK, Release Mode switch to SERIE (default).
2. Set QFE on altimeter to value shown in kneeboard for target waypoint.
3. Default bomb approach altitude is 60 m AGL (internal radar altimeter). To change:
  1. Set Targeting Mode switch to VALB (default). (If set to STD, height will be 60 m.)
  2. Set TAKT - IN.
  3. Enter 91, then three digit altitude in m (30 to 500 m).
     910300 = 30 m, 915000 = 500 m. Default is 60 m (or 910000).
  4. Press LS, then set AKT POS - OUT.
4. Default bomb pattern is Compact, both bombs burst over same location. Bomb patterns only work if dropping both bombs in SERIE. To change:
  1. Set TAKT - IN, then enter:
    - 921000 for Long (bombs burst in line one after the other)
    - 922000 for Wide (bombs burst next to each other)
    - 920000 for Compact (default)
  1. Press LS, then set AKT POS - OUT.
2. When approaching target waypoint, set Master Mode dial to ANF.
3. Speed 0.6 to 0.9 Mach. Use Stage 2 AB for about 0.85 Mach.
4. Height 50 m to 500 m.
5. Hold trigger UNSAFE to show HUD symbology.
6. Distance bars will appear at bottom of HUD. When horizontal line is within the outer vertical bars, target is in range. Max range is about 6 to 7 km at 0.9 Mach
7. Hold down trigger to release. First bomb will release about 1.3 seconds after trigger is held, second one will be 1.5 sec later. You must press the trigger again to drop the second pair if you're carrying 4.

Other weapon info
- RB 24 = AIM-9B (rear aspect)
- RB 24J = AIM-9J or AIM-9P3 (rear aspect, but longer range and better seeker)
- RB 74 = AIM-9L (all aspect)
- RB 75 = AGM-65A Maverick (E/O seeker)
- RB 75B = AGM-65B Maverick (magnified optics, but not used IRL?)
- RB 75T = AGM-65A Maverick with heavier warhead
- RB 04E = Old antiship missile
- RB 15F = Newer antiship missile
- RB 05A = Manually guided A2G missile
- BK 90 Mjolnir = Glide cluster bomb, 6 km max range, 50-500 m drop height