1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Cold Start

(manual is much faster than auto)
Cold Start using Direct Engine Start (no separate APU start)
Canopy ... Close (shift-T7 forward)
Left console behind throttle, back to front:
1. Fuel Shutoff Lever ... DOWN (big yellow lever on back wall)
2. DECS switch ... ON (just above Fuel Shutoff Lever)
3. OXY (Oxygen) switch ... OXY (forward position)
4. PUMP (fuel pump) switches ... NORM (forward position)
Left console in front of throttle, back to front:
1. RPS/YAW switch ... ON (middle position)
2. ANTISKID switch ... ON (middle position)
3. Flaps Power switch ... ON (middle position) (under flaps switch)
Positions as noted:
1. BATT switch ... BATT (forward position) (right console front)
2. Left and Right MFDs, HUD, and UFC ... ON (HUD knob is under UFC with other HUD controls)
3. Throttle ... Fully Aft (if you push it past the idle detent, press Bottom Thumb Button to pull it back)
4. ENG ST (Engine Start) switch ... ENG (right console front)
5. At 9% RPM ... Throttle to Idle (push throttle forward over detent, then pull back to detent)
6. Engine should stabilize at about 28-29% RPM.
7. Master Warning light ... Reset if needed (press)
8. Nozzle position lever ... 10 degrees
9. Ejection Seat ... Arm (push down lever sticking forward out of right hand side of seatback)
10. Left MFD ... EHSD page (Dish Hat left)
11. Align INS (using SAVED HEADING or PRE-ALIGNED setting in Special settings tab):
  Ground alignment
  1. INS knob ... INS GND (center console bottom)
  2. When EHSD page shows QUAL 0.7 OK, set INS knob to IFA if year is 1986 or later, or NAV if earlier
  Carrier alignment
  1. Only if using SAVED HEADING: Ground crew .. Ground Electric Power Connect (connects SINS data cables)
  2. INS knob ... SEA (center console bottom)
  3. When EHSD page shows QUAL 0.7 OK, set INS knob to IFA if year is 1986 or later, or NAV if earlier
  4. Only if using SAVED HEADING: Ground crew ... Ground Electric Power Disconnect
1. After setting INS to IFA/NAV, Master Caution INS warning should go away on its own in a few seconds.
1. FLIR switch ... FLIR (center console bottom)
2. DMT switch ... DMT (center console bottom)
3. PROBE HEAT switch ... AUTO, or PRB HT if near freezing at ground level (center console bottom)
4. Radios 1 and 2 ... ON and adjust volume (UFC)
5. ICS Ground Volume knob (larger outer knob) ... ON and adjust volume (Bitchin Betty volume, maybe other sounds) (right console middle)
6. ICS Aux Volume knob (smaller inner knob) ... ON and adjust volume (volume for Sidewinder and Sidearm) (right console elbow)
7. Ground crew ... Remove wheel chocks

Proceed with pre-flight checklist on next page.