1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

202 - Ground - Preflight, Jettison, Performance Limits

Preflight (hot start or auto started)
1. Lights ... INST PNL and CONSL knobs as desired (right console)
2. BINGO fuel amount ... As desired (fuel panel above right knee), 2500 lbs is a good default
3. ECM knob ... RCV for automatic jamming (if carrying a jamming pod) (instrument panel right side)
4. EXP knob ... AUT (for chaff/flare) (instrument panel right side)
5. RWR knob ... ON and adjust volume as desired (I usually set to minimum volume that is still ON) (instrument panel right side)
6. Power up TPOD ... If carrying TPOD, on right MFD, go to Menu, TPOD OSB, STBY OSB (to OPER), warmup takes 3 minutes for TV camera, 6 to 8 minutes to cool the FLIR (F-NOTRDY message).
7. Engine Panel (EDP) brightness knob ... As desired (instrument panel right side)
8. Radar altitude warning ... As desired, default is 500 ft
  - To change, press ALT button on UFC, enter new altitude on keypad, press ENT.
1. Set up EHSD map ... On left MFD, go to Menu, EHSD OSB, MAPM OSB, COLOR OSB (B4 OSB) to cycle color until page is readable in VR, then MAPM again to return to main controls??
2. Align/Warm up weapons ... On left MFD, go to Menu, STRS page, select weapons as needed to start alignment/warmup. JDAMs may need up to 8 minutes, Mavericks need 3 minutes. Do not select any other weapon until they are ready.
3. Nozzle position ... 10 degrees (Flaps lever on throttle).
4. Set laser codes for GBU/LDJAM and APKWS with built-in kneeboard page.

Performance limits
- Fuel: 7759 lbs internal
  - with 2x drop tanks (2003 lbs ea.) = 11764 lbs; with 4x drop tanks (2003 lbs ea.) = 15700 lbs
- Wingborne flight: 120 kts
- Flaps STOL: max 300 kts and nozzle position min 25 deg
- Landing Gear: 250 kts
- Rolling speed on ground: 180 kts
- Refueling probe extended: 300 kts
- Under 1 g: 15 seconds max
- Engine time limits:
  - Mode	RPM	JPT	Time	Notes
  - Max VTOL wet	120.0%	800 °C	15 secs	"15 seconds" warning voice
  - Max VTOL dry	113.5%	780 °C	15 secs	"15 seconds" warning voice
  - Normal VTOL wet	116.0%	780 °C	1.5 mins
  - Normal VTOL dry	111.0%	765 °C	2.5 mins
  - Combat	111.0%	750 °C	10 mins	Toggle with Front Thumb Button
  - Max	109.0%	710 °C	15 mins
  - Max continuous	102.0%	645 °C	unlimited
  - At least one minute of Max or Max Continuous between times of Combat thrust use.
  - Don't use water injection below 5 °C ambient temp or over 10000 ft.
- Climb: Simplified best climb is to start climbing at 300 KCAS until interception of Mach number based on Drag Index (VREST page shows DI), then maintain that Mach to altitude.
DI	0	10	20	30	40	50	60	70	80
Mach	0.80	0.77	0.74	0.71	0.68	0.65	0.63	0.60	0.59