1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - VREST page and weight limits

VREST page
- Shows aircraft weight and limits for Vertical Landing, Vertical Takeoff, and Short Takeoff. VREST menu option is only visible in NAV or VSTOL Master Mode.
- Base page
  - BAW ... Basic aircraft weight without fuel or water (always 14304 lbs in DCS??)
  - H2O ... Water weight (500 lbs when full)
  - BDI ... Basic Drag Index
- VL (Vertical Landing) and VTO (Vertical Takeoff) pages
  - Identical except that VL calculates based on 95% of max hover performance and VTO calculates based on 97% of max hover performance. You have more performance with the VL weight.
  - F+W ... Maximum combined weight of onboard fuel and water allowed for vertical landing/takeoff with current stores. Changes as you drop stores. Dump fuel or stores to make numbers match your actual fuel and water amounts.
- STO (Short Takeoff/Landing) page
  - NRAS ... Nozzle Rotation Airspeed (kts) - Airspeed at which to rotate nozzles.
  - NOZ ... Nozzle Angle (deg) - Set Nozzle Stop Lever to this value.
  - GROL ... Ground Roll distance (ft)
  - DT50 ... Distance to clear 50 ft obstacle (ft)
  - ASPD ... Abort Speed (kts)
  - SDST ... Stopping Distance (ft)
  - OATC/OATF ... Outside Air Temperature (deg C or F)
  - ALTM ... Altimeter pressure setting (inHg)
  - FELV ... Field Elevation (ft)
  - GWT ... Gross Weight (lbs) - Current total weight??
  - RUNW ... Runway Data - Use UFC OSBs to change values if needed.
  - GWIND ... Ground Wind Data (heading/speed in kts) - Use UFC OSBs to change values if needed.
- CRUS (Cruise) page
  - Columns show ACR (current Altitude Cruise) and OPCR (Optimum Altitude Cruise)
    - * means current altitude is higher than optimum altitude
    - Some values can be set with the UFC OSBs to calculate cruise at different speeds/altitudes.
  - CAS ... Airspeed in kts for best range at current or optimum altitude.
  - MACH ... Mach for best range at current or optimum altitude.
  - CALT ... Current (refreshes every couple seconds) or optimum altitude.
  - RANG ... Range at current or optimum altitude if flying at recommended cruise speed.
  - RFUL ... Remaining fuel.
  - MRNG ... Max Range you can reach if going at current or optimum altitude and speed, with 800 lb reserve.
  - WIND ... Wind heading/kts at current or optimum altitude.
  - GWT ... Current Gross Weight.
  - DI ... Current Drag Index.

Tested Max Weights
STO
- Max weight (as of 2.7.0 with the less-powerful engine):
  - For FARP pad grass strip at sea level, 23268 lbs (100% fuel, gun, TGP, 2x IR Mav, 2x APKWS, 2x AIM-9M) is just possible. No limit for longer runways.
Vertical Takeoff
Max weight (as of 2.7.0 with the less-powerful engine):
  - Absolute max at sea level is 21500 lbs, barely climbs, use with extreme caution.
  - Reasonable max is 21000 lbs wet, 20000 lbs dry, allows climbing above obstacles.
  - 2000 ft = 20500 lbs??, 3000 ft = 19750??, 4000 ft = 19000 lbs
  - Temperature doesn't seem to make a difference, although it should...