1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

303 - Flight - Takeoff

Conventional Takeoff
1. Master Mode ... VSTOL (B5 button)
2. Parking brake lever ... Forward (also unlocks throttle) (Pinky Wheel forward). Plane rolls forward.
3. Hold Flip-down Trigger to use NWS.
4. Taxi to takeoff position.
5. Nozzle Stop Lever ... Fully aft (Top Hat Ring forward/back)
6. Nozzle Position lever ... 10 deg (Flaps lever)
7. Flaps ... AUTO (T6 switch)
8. Water Injection switch ... As needed (use for max loads or hot-and-high conditions) (T7 switch)
9. Anti-Skid Switch ... ON (default)
10. Airbrake ... Retracted
11. Go to full throttle.
12. Rotate carefully at 135 kts to 165 kts, no more than 180 kts, put Witches Hat at pitch carets (6 deg nose up). Avoid roll or sideslip.
13. When airborne, retract the landing gear.
14. Reduce throttle to 102% or less.
15. Set Nozzle Position lever to 0 deg (fully forward).
16. Turn off Water Injection (T7 switch)
17. Nozzle Stop lever ... Fully aft (Top Hat Ring forward/back)

Short Takeoff and Ship Takeoff
See VREST and weight limits kneeboard page for max weights.
1. Master Mode ... VSTOL (B5 button)
2. Parking brake lever ... Forward (also unlocks throttle) (Pinky Wheel forward). Plane rolls forward.
3. Hold Flip-down Trigger to use NWS.
4. For very tight turning, set ANTISKID switch to NWS. Then hold Flip-down Trigger for NWS HI.
5. Taxi to takeoff position.
6. Nozzle Stop Lever ... 60 deg (60 deg label should be visible, but no higher labels) (Top Hat Ring forward/back)
7. Nozzle Position lever ... 10 deg (Flaps lever)
8. Flaps ... STOL (T6 switch)
9. H2O switch ... As needed (use for max loads or hot-and-high conditions) (T7 switch)
10. Anti-Skid Switch ... ON (default)
11. Airbrake ... retracted
12. Go to full throttle.
13. At 100 to 110 kts, or when at the end of the ship's deck, pull Nozzle Position lever back so it hits the stop (60 deg).
14. When airborne, retract the landing gear.
15. When over 120 kts (wingborne flight), reduce throttle to 102% or less.
16. Start moving the Nozzle Position lever forward slowly to gain speed.
17. If using STOL flaps, retract flaps before exceeding 300 kts or using less than 25 degrees of nozzle.
18. Turn off Water Injection (T7 switch)
19. Nozzle Stop lever ... Fully aft

Vertical Takeoff
See VREST and weight limits kneeboard page for max weights.
1. Master Mode ... VSTOL (B5 button)
2. Parking brake lever ... Forward (also unlocks throttle) (Pinky Wheel forward). Plane rolls forward.
3. For very tight turning, set ANTISKID switch to NWS (left console front vertical panel, next to gear lever). Then hold Flip-down Trigger for NWS HI.
4. Nozzle position lever ... 82 deg (vertical flight) (Flaps lever)
5. Nozzle stop lever ... Fully aft (Top Hat Ring back until fully aft)
6. Flaps ... STOL (T6 switch)
7. H2O (Water Injection) switch ... TO (Take Off, up position) (T7 switch)
8. ANTISKID switch ... ON (default) (left console front vertical panel, next to gear lever)
9. Airbrake ... retracted
10. Go to full throttle.
11. When airborne, turn into the wind if possible. Avoid sideslip.
12. Retract the landing gear.
13. When over 25 ft and clear of obstacles, put Witch Hat on Pitch Carets (6 deg nose up) and start moving the Nozzle Position lever (Flaps Lever) forward slowly to gain speed.
14. When over 120 kts (wingborne flight), reduce throttle to 102% or less.
15. Retract flaps before exceeding 300 kts or using less than 25 degrees of nozzle position.
16. Turn off Water Injection (T7 switch)