1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

304 - Flight - Landing

All landings
1. Master Mode ... VSTOL (B5 button)
2. Nozzle Stop lever ... Fully aft (Top Hat Ring back until fully aft) or you'll be sorry

Conventional Landing
1. Nozzles ... 0 deg (Flaps Lever)
2. Under 250 kts, gear down and flaps AUTO.
3. Approach angle/glideslope should be 3 degrees.
4. Put Witches Hat 2 deg above horizon (Pitch Carets are at 6 degrees).
5. Don't pitch up too much or you'll tailstrike. (6 degrees max??)
6. Nozzles full back for braking.
7. Post-flight:
  1. Parking brake on (idle throttle, then Pinky Wheel back)
  2. Nozzles to 10 deg.
  3. Flaps to STOL.
  4. Retract airbrake.

Rolling Vertical Landing -- Allows more weight than a vertical landing but requires some rollout
Desired Touchdown Speed (KCAS)	Maximum allowed weight
<= 45 kts	VL weight
50 kts	VL + 2300 lbs
55 kts	VL + 2700 lbs
60 kts	VL + 3100 lbs
65 kts	VL + 3500 lbs
70 kts	VL + 4000 lbs

1. Under 250 kts, gear down and flaps AUTO.
2. Set nozzle angle as required to maintain desired speed.
3. Adjust power to intercept glideslope to touchdown (3 to 6 degrees).
4. Put Witches Hat 2 deg above horizon (Pitch Carets are at 6 degrees).

Vertical Landing
See VREST and weight limits kneeboard page for max weights.
  - Dump fuel if needed to make weight, switches are on the left console behind throttle, they will dump until fuel reaches your set BINGO amount. Fuel dump takes a while so start early.
1. Start slowing down at least a couple miles out. Under 300 kts, put down STOL flaps. Set nozzles to around 60 deg to help slow down.
2. Under 250 kts, put down gear.
3. Final approach at a couple hundred feet, maybe 100 kts?
4. Put nozzles to 82 deg (vertical flight) a few hundred yards before the landing pad.
5. Put Witches Hat on the horizon to hover.
6. Fly it kind of like a helicopter, but it's a lot less responsive. Don't get angled more than a few degrees in any direction. Don't sideslip. Control altitude with throttle, watching the velocity vector. Big, quick stick movements in the direction you want to correct, and then quickly move stick back to center, may work better than trying to be slow and gentle.
7. Set down as gently as possible. Witches Hat on horizon is slightly nose high so don't be surprised by a pitch down onto the nosewheel when touching down.
8. Apply brakes to keep from rolling away.
9. Post-flight:
  1. Parking brake on (idle throttle, then Pinky Wheel back)
  2. Nozzles to 10 deg.
  3. Flaps to STOL.
  4. Nozzle stop lever fully aft.

Ship Vertical Landing
1. Set TACAN to carrier's channel for approach (see steps in Navigation kneeboard page).
2. Contact carrier and request landing. Carrier will respond with BRC (Base Recovery Course, the heading of the carrier itself). Set that as a Course in the EHSI for reference.
3. Call "See you at 10" when 10 miles out. There may be other communication needed as well.
4. Fly the pattern (left as an exercise to the reader).
5. Generally, follow steps for Vertical Landing above.
6. Basic idea is to approach from the stern, but offset slightly to port so you're not over the deck.
7. Come up on the port side, match speeds with the ship, be about 20 ft higher than the deck.
8. When you're even with a landing spot and matched speed with the ship, gently side slip to the right over the deck and touch down.