1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

305 - Flight - Waypoints, Markpoints, Targetpoints

General info about Waypoints, Markpoints, and Targetpoints
- Waypoints ... W0-W60, W0 is your starting location
- Markpoints ... M0-M29 (M30 is same as M0??)
- Targetpoints ... T0-T10, T0 is a special system targetpoint:
  - T0 is set to the aimpoint (CCIP point, rocket pipper point, etc.) when a weapon is fired.
  - Long-press Lower Gray Button to set T0 to the current designated point in the TPOD, and select it as the navigation destination. That also brings up the Quick Access Menu on the UFC ODU to select between the types of points.
- Steer To Point (STP) ... The currently selected point for navigation, shown on EHSD between the up/down arrows. Distance and bearing to STP are shown in the HUD?? Maverick range and JDAM DLZ are shown relative to the Steer To Point, not necessarily the target designation.

Lower Gray Button (WINC/Waypoint Increment) functionality
- Press Lower Gray Button to cycle through your currently selected point type (either waypoints, markpoints, or targetpoints).
- With no target designation (EHSD DESG OSB unboxed), long-press Lower Gray Button to open the Quick Access (QA) mode on the UFC ODU, then select WYPT, MKPT, or TGPT, (optionally enter the number of point you want to select on the UFC keyboard,) and press ENT. Now pressing Lower Gray Button will cycle through that type of point.
- With a target designation (EHSD DESG OSB boxed), long-press Lower Gray Button to open the Quick Access (QA) mode as above, and also to save the target location to T0, and set T0 to be the current Steer To Point (STP).
- Note: On EHSD page, when DATA is boxed, waypoint up/down arrows increment through all point types, but this is for display/editing them, and doesn't change your active navigation selection.
  - You can also long-press the up/down arrow OSBs on the EHSD page to enter QA mode.

Create a new waypoint or Edit a waypoint by entering coordinates
1. On EHSD page, press DATA OSB to box.
2. On UFC keypad, enter number of waypoint to be created or edited, or 77 to create a new waypoint after the last one, then ENT. (New waypoint number will be shown with "*" on display.)
3. Enter the waypoint coordinates as either lat/long or MGRS:
Using latitude/longitude:
    1. Press POS UFC OSB (subsequent presses toggle between lat and long).
    2. Press 2 for N or 8 for S, then latitude in DDMMSS format, then ENT.
    3. Press 4 for W or 6 for E, then longitude in DDDMMSS format (note leading zero if needed), then ENT.
Using MGRS grid:
    1. Press UTM UFC OSB to show surrounding grids on other OSBs (subsequent presses show more surrounding grid squares).
    2. Select grid square by pressing corresponding UFC OSB.
    3. Enter coordinates on UFC keypay and press ENT.
1. Altitude is automatically set to ground level, change if needed by pressing the ALT ODU OSB.
2. On EHSD page, press DATA OSB to unbox and stop editing.

Waypoint offsets, useful if you know a target bearing and distance from a waypoint
1. On EHSD page, press DATA OSB to box.
2. Press WYPT ODU OSB to change to WO/S (Waypoint OffSet).
3. Press BRG ODU OSB, then enter bearing on keypad, then ENT.
4. Press RNG ODU OSB, then enter range on keypad, then ENT. Numbers less than 100 are interpreted as nmi, numbers greater than 100 are interpreted as meters.
5. On EHSD page, press DATA OSB to unbox and stop editing.
6. Now when you have the waypoint with the offset selected, press the WO/S OSB to box it and track the offset instead of the waypoint itself.

Create Waypoint, Markpoint, or Targetpoint with TOO button
If you have a designation (EHSD DESG OSB boxed), TOO will store the designated point. If you don’t have a designation (EHSD DESG OSB is unboxed), TOO will store the location of your airplane at the moment TOO was pressed.
1. Press TOO button on UFC.
2. Select WYPT, MKPT, or TGPT (default) on UFC ODU.
3. Optionally, enter the point number you want to store. The next available point number is selected by default.
4. Press ENT to store the point.

Create Markpoint with MKn button
Press MKn OSB on EHSD page. Creates Markpoint on the ground at your current aircraft location. MK1 stores in Markpoint 1, etc.