1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

305 - Flight - Navigation, EHSD

Navigate to Waypoints, Markpoints, and Targetpoints
1. Press Lower Gray Button (WINC/Waypoint Increment) to cycle through your currently selected point type (Waypoints, Markpoints, or Targetpoints), or use Waypoint Inc/Dec OSBs on ESHD page. Long-press the Waypoint Inc/Dec OSBs to skip to next category (waypoint/markpoint/targetpoint)??
2. To change the type of point you have selected, Long-press Lower Gray Button to open the Quick Access Menu on the UFC ODU, then select WYPT, MKPT, or TGPT, optionally enter the number of point you want to select on the UFC keyboard, and press ENT. Now pressing Lower Gray Button will cycle through that type of point.

Navigate to TACAN beacon
1. Tune TACAN:
  1. Press TCN button on UFC.
  2. Enter TACAN channel number on keypad and press ENT.
  3. On the UFC ODU, select the X or Y channel, and T/R or A/A mode.
  4. Press ON/OFF button on UFC to turn TACAN on.
2. On EHSI page, TACAN bearing and range shows in the upper left corner. Press TCN OSB to put the steering info in the HUD (NAV master mode only??).

AWLS (ILS)
1. TODO
2. Must be in STOL or NAV mode for the option to show in the EHSD page.

EHSD page use
Change text color for better visibility
Press MAPM OSB to box, then COLOR OSB (B4 OSB) to cycle colors.
Slewing waypoint with TDC
1. Press DATA OSB to box.
2. Press POS UFC OSB.
3. Press Dish Hat forward to set TDC to INS.
4. Press SCL OSB to unbox and set desired zoom. Slew moves faster when zoomed out, slower when zoomed in.
5. Use TDC slew to move the waypoint on the EHSD map. All movement is saved immediately!
6. On EHSD page, press DATA OSB to unbox and stop editing.
DESG OSB functionality
- When DESG is boxed, the currently selected Steer To Point (waypoint, markpoint, or targetpoint) is selected as the designated target, and the TPOD is automatically cued to that point.
- If it says DESG STP, the currently selected Steer To Point is still the designated target. If it says DESG TGT, the targeted point has moved away from the Steer To Point.
- Weapon release parameters (e.g. JDAM DLZ, Maverick range indicator) are made relative to the Steer To Point point, which may not be the same as the DESG point (unless it says DESG STP).
- If DESG is boxed, long-pressing Lower Gray Button will automatically set the target point (as designated through TPOD or DMT) to T0 and will select T0 as the Steer To Point point.
- To re-cue the TPOD back to the selected waypoint, un-box and re-box DESG.