1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

308 - Flight - Jettison, Countermeasures, ECM

Jettison
1. Emergency Jettison button (black and yellow striped, far outboard) drops everything except A2A missiles.
2. Selective Jettison knob on Armament Control Panel does regular jettison. Set knob sleeve to desired category, then press center red JETT button.
  - STA = Individual stores selected with small round buttons under station numbers, also drops ejector racks.
  - STOR = Same as STA but keeps ejector racks.
  - SAFE = No jettison.
  - CMBT = Everything but A2A missiles, including ejector racks (same as Emergency Jettison button).
  - FUEL = External tanks.

Countermeasures dispensing and programs -- WIP
Countermeasures hat commands:
  - F: Chaff, dispensed according to CHF mode (S or P)
  - B: Flares, dispensed according to FLR mode (S, P, M, G, or R)
  - P: Both chaff and flares, always dispensed according to the ALL program (default 1x chaff and 1x flare)
  - U: ECM mode RCV (jamming only when detected/locked)
  - D: ECM mode RPT (jamming always on)
EXP (Expendables) knob (right side of instrument panel):
  - OFF ... Dispensers turned off, will not dispense any countermeasures
  - AUT ... Dispensers will cycle, one countermeasure coming out of each (two on top, two on bottom). (In real aircraft, AUT mode will select dispenser based on altitude and attitude.)
  - UP ... Countermeasures only come out of upper dispensers (may be useful for low altitude flight).
  - DWN ... Countermeasures only come out of lower dispensers (may be useful for high altitude flight).
  - RWR ... Not implemented (effectively same as OFF??)
  - Recommended to always set to AUT mode.
1. Countermeasures modes and programming:
  1. Go to the EW page: Menu OSB, EW OSB, or Dish Hat Left 3x to cycle left MFD screens.
  2. Set dispenser mode with CHF and FLR OSBs on left (L1 and L2 OSBs). Dispenser modes:
    - S ... Single, fires a single CM per button press, cycling through selected dispensers.
    - P ... Program, fires the CM program, cycling through selected dispensers.
    - M ... (only available for flares) Multiple, fires a single CM from each dispenser simultaneously.
    - G ... (only available for flares) Group, fires the CM program from each dispenser simultaneously.
    - R ... (only available for flares) Unknown, seems to be the same as S?
    - Recommended to always set both to P.
1. Countermeasures programming:
  1. On EW page, press PROG OSB.
  2. Select CHF or FLR on top OSBs, then change program settings with UFC ODU OSBs.
  3. Select ALL OSB on top to change program settings for ALL program (Countermeasures Hat press, real aircraft countermeasures hat right). This is separate from the non-ALL programs.
  4. Press PROG OSB again to exit programming mode.

ECM jammer
- RCV mode is jamming only when detected/locked.
- RPT mode is jamming always on.
- Average SAM range in RPT mode, vs range with no jamming (closer to 100% means less effective jamming), tests from Pukin Dog video https://youtu.be/C-fS6BHMDBE:
SAM	RCV mode	RPT mode
SA-2	81%	73%
SA-3	95%	95%
SA-6	92%	93%
SA-8	89%	85%
SA-10	97%	97%
SA-11	80%	74%
SA-15	63%	63%