1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - Guns, Rockets, Unguided Bombs

Master Arm ... ON (B2 button to toggle)
Master Mode ... A/G (B1 button)

Guns
1. Select GUN on with OSB buttons at top of left MFD.
2. As soon as pipper starts unwinding, you're in range.
3. IMPORTANT: Throttle must be over 68% to fire! Nozzles must be 30 deg or less!
4. Fire with Trigger.

Rockets
1. Select rockets with OSB buttons at top of left MFD.
2. Set up Armament Control Panel under left MFD:
  - MODE ... CIP for CCIP
  - FUZ ... -- -- (fuze has no effect)
  - QTY ... Number of rockets to fire per pod per impulse.
  - MULT ... Number of pylons to fire rockets from per impulse (1, 2, or 4).
- Total rockets fired per impulse will be QTY x MULT.
  - INTV ... 000 (no effect)
1. As soon as pipper starts unwinding, you're in range.
2. Fire with Red Button.
3. You can also fire gun with Trigger. Gun crosshair is "+" shown on HUD.

CCIP bombing
All
1. Select bombs with OSB buttons at top of left MFD.
2. Set mode, fuze, and ripple on Armament Control Panel under left MFD.
  - MODE ... AUT for CCRP, CIP for CCIP
  - FUZ ... NT IN for most bombs.
  - QTY ... Number of release impulses.
  - MULT ... Number of pylons to drop from per impulse (1, 2, or 4).
- Total bombs dropped will be QTY x MULT.
  - INTV ... As desired, interval between bombs in 10s of ft.
1. CCIP impact point is dashed cross at bottom of bomb fall line.
2. Press Red Button to drop bombs.
A short horizontal line across the bomb fall line is the "reflected cue"; actual bomb impact will be below the HUD. In that case, put CCIP cross on target, press and hold pickle, and bomb will be dropped in CCRP mode at the correct moment.
- Whenever the pickle is pressed in CCIP mode (even if a bomb doesn't drop), the Target Point is updated to the CCIP impact point and the DMT is slaved to that point.
- When you have a Target Point designated, you can press Uncage to toggle from CCIP to CCRP mode??
Mk 20 Rockeye
- FUZ ... PR or OP, no apparent effect on result, always the same burst height and pattern size.
  - IRL, PR should be "Primary", meaning bomb bursts after 1.2 seconds; OP should be "Option", meaning bomb bursts after 4.0 seconds. However in game, Rockeyes seem to burst based on altitude AGL, from 400 to 700 ft.
- Low altitude level release (~450 kts, 400 ft) with CCIP falls very short of aim point. Put target at about double the CCIP cross depression.
Mk 82 Snakeye and AIR
Slick or retarded is selected by separate MFD buttons for 82HD (High Drag/retarded) or 82LD (Low Drag/slick). Not sure if FUZ setting matters.

CCRP bombing
1. See TPOD page and LGB/JDAM page to see how to designate a target using EHSD DESG OSB which enables AUTO mode.
2. Line up with the bomb fall line and fly toward the target.
3. 6 seconds before drop, the drop cue horizontal line will appear at the top of the bomb fall line.
4. A few seconds before drop, the drop cue will fall down the bomb fall line. Hold the pickle, bombs will release when drop cue reaches the velocity vector.