1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - TPOD use

Master Arm ... ON (B2 button to toggle)
Master Mode ... A/G (B1 button)

Very short version:
1. Right MFD: Menu, TPOD OSB, STBY OSB (to OPER), SAFE OSB (to ARMED), TRNL OSB (to LASR), ish Hat double-press (2nd line on MFD should say TPOD).
2. Left MFD: Menu, EHSD OSB; if using laser: CODE OSB, enter laser code on UFC; if using AUTO/CCRP bombing, press DESG OSB (to boxed)
3. Slew TPOD crosshair, long-press Lower Gray Button to set targetpoint T0 to target. Dish Hat left to toggle FOV, Middle Finger Hat up/down to zoom, Pinky Button to fire laser, Dish Hat long-right to toggle CCD/FLIR, Dish Hat right to toggle WHOT/BHOT, Dish Hat down to cycle tracking mode.
4. In order to arm laser, all of these must be true, else laser will be set to SAFE: landing gear up, airspeed > 100 kts, Master Arm ARM, Master Mode A/G, TPOD SWFOV mode OFF, TPOD in AREA or POINT lock or slaved to a System Designation.

TPOD use
1. On right MFD, press Menu, TPOD OSB. If no picture, press STBY OSB (to OPER).
2. Press Dish Hat double-press to put TPOD into right MFD and set as SOI (TDC controls TPOD).
  IMPORTANT AND POTENTIALLY CONFUSING:
  - If TPOD is already in right MFD, Dish Hat double-press will cycle TDC control of TPOD or TV/INS (DMT), as shown in second line below OSBs at the top of the right MFD.
  - When TDC is controlling TPOD, Dish Hat U/D/L/R controls TPOD functions (see below).
  - When TDC is not controlling TPOD, even if TPOD video is showing, Dish Hat U/D/L/R has normal HOTAS functions.
1. If using laser (all controls on TPOD MFD unless otherwise noted):
  1. Set laser code:
    - IMPORTANT: Laser code is reset whenever there's weight-on-wheels.
    1. In A/G master mode, on EHSD page, press the CODE OSB.
    2. Enter code on UFC and press ENT button on UFC.
  2. Press SAFE OSB on top row left so it says ARMED.
  3. Press TRNL OSB on top row so it says LASR. Other modes are TRNL (training), MRKR (marker), D+M (designator and marker), EYES (eye-safe laser designator to protect ground troops)
  4. To fire laser, press FIRE OSB on top row so it's boxed or press Pinky Button (mapped to that OSB). Laser can be fired continuously.
2. Controls: With TPOD on MFD and TDC controlling TPOD, control TPOD functions with Dish Hat:
  - U: Toggles LTIP mode (some kind of special laser ranging mode, not fully modeled??)
  - D: Cycles between AR (Area track), PT (Point track), and MT (Moving target, same as PT for now) modes. PT and MT will automatically "snap" to targets, AR will not.
  - D-L: Selects INR (inertial track) mode (not sure what this does??)
  - L: Toggles NFOV/WFOV
  - L-L: Enters LSS (Laser Spot Search) mode
  - R: Toggles WHOT/BHOT in FLIR mode
  - R-L: Toggles CCD/FLIR mode
  - On throttle, Pinky Button to toggle laser (mapped to OSB 8) and Middle Finger Hat up/down to zoom (mapped to OSB 3 and 4).
  - Press Flip-down Trigger 2x to undesignate (1st press) and slave TPOD to VV (2nd press).
1. Designate a target for AUTO (CCRP) bomb drops, including GBUs and JDAMs:
  1. Put INS system into Designation mode:
    1. Go to EHSD page on left MFD.
    2. Make sure WYPT OSB is boxed.
    3. Press DESG OSB. Should say DESG STP. This creates a target from the current waypoint.
  2. CCRP steering symbology should appear on HUD, and bomb can be dropped.
  Note that targeting symbology is distinct from navigation symbology. The INS will always navigate to the steerpoint (either a waypoint, or a target point, which is not the same as a target designation). You can set target point T0 to the current target designation at any time by Long-Press Lower Gray button on the joystick.
  1. You can now move/redesignate the target using any aircraft sensor (TPOD, DMT, etc) and the steering symbology should move to follow the new target position, and the EHSD will say DESG TGT. This means the steerpoint (navigation symbology) is not at the same place as the target (target symbology).
  2. If "Unrealistic TDC behavior" box in Options is checked (recommended), when slewing the TPOD, the target point will be updated automatically to the crosshairs as soon as you stop slewing.

Valid laser codes:
Format is ABCC, A=1, B=1-7 (or 1-6 in DCS??), C=1-8, never 0 or 9. Range should be 1111 to 1788 but may be 1111 to 1688 in the game. Some planes in DCS (A-10C?) may not be able to set B=7.