1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

503 - A/G - APKWS, LGB

Master Arm ... ON (B2 button to toggle)
Master Mode ... A/G (B1 button)

TPOD summary (see dedicated TPOD page for details):
1. Right MFD: Menu, TPOD OSB, STBY OSB (to OPER), SAFE OSB (to ARMED), TRNL OSB (to LASR), Dish Hat double-press (2nd line on MFD should say TPOD).
2. Left MFD: Menu, EHSD OSB; if using laser: CODE OSB, enter laser code on UFC; if using AUTO/CCRP bombing, press DESG OSB (to boxed)
3. Set laser code: In A/G Master Mode, go to EHSD page, press CODE OSB, enter code on UFC, press ENT.
4. Controls (these only work if the TPOD MFD says TPOD on the second line!):
  - Slew ... TDC stick
  - Set targetpoint T0 to target ... long-press Lower Gray Button (used for CCRP/AUT bombing)
  - Toggle NFOV/WFOV ... Dish Hat left
  - Zoom ... Middle Finger Hat up/down
  - Toggle CCD/FLIR ... Dish Hat long-right
  - Toggle WHOT/BHOT (FLIR only) ... Dish Hat right
  - Cycle tracking mode (Area/Point/Moving) ... Dish Hat down
  - Toggle laser firing ... Pinky Button

APKWS laser guided rockets with TPOD -- HE is HE, MPP is anti-armor
1. IMPORTANT: APKWS laser code can only be changed on the ground with engine off (default is 1688). Kill engine with Bottom Thumb Button. Open kneeboard to page showing laser code and hotkeys to change. Change code as needed. Start engine with ENG ST switch to ENG (right console front), at 9% RPM push throttle over detent, then back to idle.
2. Power up TPOD, arm laser, set laser code. IMPORTANT: Laser code is reset whenever there's weight-on-wheels.
3. Select rockets with OSB buttons at top of left MFD.
4. On Armament Control Panel:
  - MODE ... CIP for CCIP
  - FUZ ... -- -- (fuze has no effect)
  - QTY ... Number of rockets to fire per pod per impulse.
  - MULT ... Number of pylons to fire rockets from per impulse (1, 2, or 4).
- Total rockets fired per impulse will be QTY x MULT.
  - INTV ... 000 (no effect)
1. Slew TPOD crosshairs onto target.
2. Press the FIRE OSB on the TPOD MFD (Pinky Button press) to toggle the laser ON.
3. When in range, press Red Button to fire rocket.
4. Max range is approx 3-5 miles from medium altitude, can be more from high altitude. After firing you can maneuver as long as the laser stays on target. Medium armored units may require multiple MPP rockets, up to 4x for Gepard. Heavy armored units like tanks are probably immune.

LGBs with TPOD
1. Power up TPOD, arm laser, set laser code. IMPORTANT: Laser code is reset whenever there's weight-on-wheels.
2. Point TPOD at target to create a target point; should automatically box DESG OSB on EHSD page and enable CCRP (AUT) bombing mode.
3. Select bombs with OSB buttons at top of left MFD.
4. On Armament Control Panel:
  - MODE ... AUT (for CCRP)
  - FUZ ... T IN or as desired
  - QTY, MULT, and INTV ... as desired
1. Fly toward CCRP line, when release cue starts falling from the top, press and hold Red Button until bombs drop.
2. There is no time-to-impact indicator so you need to guess when the bomb is close, or lase the whole time.
3. Press the FIRE OSB on the TPOD MFD (Pinky Button press) to toggle the laser ON.