1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

504 - A/G - JDAM, LJDAM

Master Arm ... ON (B2 button to toggle)
Master Mode ... A/G (B1 button)

TPOD summary (see dedicated TPOD page for details):
1. Right MFD: Menu, TPOD OSB, STBY OSB (to OPER), SAFE OSB (to ARMED), TRNL OSB (to LASR), Dish Hat double-press (2nd line on MFD should say TPOD).
2. Left MFD: Menu, EHSD OSB; if using laser: CODE OSB, enter laser code on UFC; if using AUTO/CCRP bombing, press DESG OSB (to boxed)
3. Set laser code: In A/G Master Mode, go to EHSD page, press CODE OSB, enter code on UFC, press ENT.
4. Controls (these only work if the TPOD MFD says TPOD on the second line!):
  - Slew ... TDC stick
  - Set targetpoint T0 to target ... long-press Lower Gray Button (used for CCRP/AUT bombing)
  - Toggle NFOV/WFOV ... Dish Hat left
  - Zoom ... Middle Finger Hat up/down
  - Toggle CCD/FLIR ... Dish Hat long-right
  - Toggle WHOT/BHOT (FLIR only) ... Dish Hat right
  - Cycle tracking mode (Area/Point/Moving) ... Dish Hat down
  - Toggle laser firing ... Pinky Button

JDAMs with TPOD, TOO mode aka Relative Targeting
1. Power up TPOD, arm laser (for ranging). No laser code is needed for regular JDAMs.
2. Point TPOD at target to create a target point; should automatically box DESG OSB on EHSD page and enable CCRP (AUT) bombing mode.
  - Use laser (Pinky Button press to toggle firing) to get range to target for maximum accuracy.
1. REQUIRED: Long-Press Lower Gray Button to set T0 target point at the designated target and make it your current Steer To Point.
2. Select bombs with OSB buttons at top of right MFD.
3. To check alignment, go to STRS page. (Alignment currently doesn't seem to be needed...)
4. Set up TERM (terminal attack) parameters if desired on UFC. (Terminal dive angle, terminal heading.)
5. On Armament Control Panel:
  - MODE ... AUT (for CCRP)
  - FUZ ... -- IN or as desired
  - QTY, MULT, and INTV ... as desired
HUD shows JDAM symbology:
  - Large circle is range indicator, triangle at bottom is max range, triangle on right half is min range.
  - N below circle means no TERM params are set, T means TERM params are set.
  - Press Uncage button to toggle use of TERM params (also toggles N/T on HUD).
  - 0 (zero) next to N or T indicates targetpoint being attacked.
EHSD also shows JDAM symbology:
  - Red bar going through your airplane shows min and max range (only appears when pointing near the target)
1. When in range, press and hold Red Button for 1.5 sec until bombs drop.
2. TDC slew to next target (no need to press TDC press if "Use EASY mode TDC" in Options is checked), pickle to drop again, slew, drop, slew, drop, etc...

LJDAMs with TPOD
WIP
1. Power up TPOD, arm laser, set laser code. IMPORTANT: Laser code is reset whenever there's weight-on-wheels.
2. (Not sure how these are different from JDAMS other than they can accept laser guidance, I'm assuming it's like dropping a JDAM, but if you're lasing, it'll follow the laser.)

Dropping multiple JDAMs on a single pass
1. TODO
2. Basically, set up multiple targetpoints either manually with TOO button or from F10 map markers.
3. Select JDAMs, then press WPN button on UFC.
4. On UFC ODUs, select targetpoints you want to drop on.
5. HUD should show all the selected targetpoints under the range symbology, in the order they will be dropped on.
6. Range circle shows range to first target. When in range, pickle. Range circle automatically changes to show range to second target, pickle, etc. If all targets are close together, you can pickle one right after the other. You might even be able to set multiple release in the weapons settings, haven't tried that.