1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

505 - A/G - Maverick

Master Arm ... ON (B2 button to toggle)
Master Mode ... A/G (B1 button)

AGM-65F Maverick (IR seeker)
Power on Mavericks. Go to STRS page, press IRMV. Cooldown takes 3 minutes. (No other weapons may be selected during that time, or cooldown will stop or restart??)
  - STRS page will show STBY in bottom left until they're ready, then will show RDY. Mavs will stay ready for 1 hour??
FUZ ... "-- IN"
Using DMT for targeting (recommended)
1. Press Dish Hat down to show DMT (in LST mode) in right MFD and Dish Hat down again to set DMT to TV mode.
2. Press TDC press to ground lock and enable slewing.
  - Press Flip-down Trigger to undesignate and toggle slaving DMT to waypoint or velocity vector.
1. TDC slew to move crosshairs to target.
2. Press Uncage button to uncage Maverick seeker and show seeker video on left MFD. Should be pointing at or near the DMT target. You're still in TV mode (shown in top left of both MFDs), which means the TDC will move the DMT crosshairs, and then the Maverick will update to the new DMT target.
3. Press Dish Hat up to set the TDC control to IRMV (shows IRMV in top left of both MFDs).
4. Now you can slew the Maverick seeker with TDC. It will automatically lock any target that gets into the center of the crosshairs.
  - Toggle Wide/Narrow FOV with Flip-down Trigger press.
  - DO NOT PRESS TDC PRESS, that will unlock and return the Maverick to boresight.
1. When locked and in range, fire with Red Button.
2. To fire next missile: Uncage, Dish Hat up, Flip-down Trigger to zoom if needed, TDC onto target, fire.
Using TPOD for targeting
NOTE: AGM-65F video cannot be seen at the same time as TPOD video. This is because the real Harrier only supports video streaming from the Maverick or the TPOD, not both at once.
1. Press Dish Hat press 2x to show TPOD in right MFD.
2. Lock TPOD on target.
3. Press Uncage button to uncage Maverick seeker and show seeker video on right MFD in place of TPOD.
4. Press Dish Hat up to set the TDC control to IRMV (shows IRMV in top left of MFD).
5. Now you can slew the Maverick seeker with TDC. It will automatically lock any target that gets into the center of the crosshairs.
  1. Toggle Wide/Narrow FOV with Flip-down Trigger press.
  2. DO NOT PRESS TDC PRESS, that will unlock and return the Maverick to boresight.
6. When locked and in range, fire with Red Button.
7. To fire next missile: Uncage, Dish Hat up, Flip-down Trigger to zoom if needed, TDC onto target, fire.

AGM-65E2/L Maverick (laser seeker) with TPOD for targeting
NOTE: Only the AGM-65E2/L works with the TPOD. The AGM-65E must be buddy-lased or used with JTAC.
Power on Mavericks. Go to STRS page, press LMAV. Gyro spinup takes 90 seconds. (No other weapons may be selected during that time, or spinup will stop or restart??)
  - STRS page will show STBY in bottom left until they're ready, then will show RDY. No indicator showing they're ready??
1. FUZ ... -- IN
2. Power up TPOD, arm laser, set laser code. IMPORTANT: Laser code is reset whenever there's weight-on-wheels.
3. Laser code on missile should be the same as the TPOD. Code is shown in the top left of the TPOD MFD.
4. Point TPOD at target but don't fire the laser yet.
5. Press Uncage button to uncage Maverick seeker. HUD will show moving X as seeker scans back and forth.
6. Fire laser (Pinky Button press); Maverick should acquire the laser. X will change into a small square box inside the TPOD target octagon when seeker acquires the laser.
  - (optional) Press Dish Hat up-long to show the Maverick seeker display in place of the TPOD for 14 seconds. TPOD will remain locked with laser firing in the background.
1. Long-Press Lower Gray Button (Waypoint Increment button) for more than 0.8 seconds to set steering to T0 (target point). This will make the HUD show correct range information for the Mav.
2. When laser is acquired and IN RNG shows on HUD, fire with Red Button.