1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

506 - A/G - Sidearm

Master Arm ... ON (B2 button to toggle)
Master Mode ... A/G (B1 button)

AGM-122 Sidearm
1. Select Sidearm by clicking weapon pylon buttons in Armament Control Panel under left MFD. (Not the STRS page on MFD.)
2. Missile starts caged. Dashed seeker circle will appear on HUD when caged.
3. Press Uncage to allow missile to fire off boresight and make seeker more sensitive. Seeker circle will be solid when uncaged.
4. When you get a high-pitched tone, missile is locked.
5. Press Trigger to fire.
6. You may need to deselect Sidearms and then reselect to clear seekers from the previous target.
As of 2.7.10, this is probably no longer possible to do...
Lofting Sidearms (numbers from Grim Reapers video):
Launch Alt	Speed	Angle	Range nmi	TOF
150	550	14°	14.5	1:46
3000	550	14°	15.4	1:58
12000	550	14°	18.5	2:33
24500	540	16°	21.6	2:20
30000	528	20°	30.0	2:28
Max ranges may be as much as 5+ nmi further than given here.

It does have at least a 9.1 nmi range, fired from 530 kts IAS, 600 ft AGL, at 15 deg angle.