1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

601 - Notes, Quirks, and Trivia

- If things are acting weird, weapons not firing, maybe some buttons not working, check that your nozzles are fully forward. Having the nozzles angled may inhibit some functions. Also make sure you're over 70% RPM, as low engine RPM also inhibits some weapons.
- The DMT can track to just inside the canopy bow left and right, for quick visual reference.
- HUD symbology:
  - Circle - Waypoint
  - Diamond - Current target/SPI
  - Octagon - TPOD target

SOI and MFDs:
- The Harrier sensor select and SOI flow works opposite, in a way, from other planes like the F-16 or F-18. In the other planes, the "Sensor Of Interest" is really the "MFD Of Interest"; you can generally have any sensor on any MFD, you select the MFD with the SCS hat, and then your TDC stick slews whatever sensor is on that MFD or moves the cursor or whatever. (And all that makes pretty good intuitive sense to me.)
- However in the Harrier, the SCS really does select the "Sensor" Of Interest, which may or may not be showing on an MFD, or might be on one that doesn't match the direction you move the SCS hat.
- SCS Down/Aft is for the DMT sensor and its modes, SCS Up is for IR Mavs, SCS Left is for the EHSI map, SCS Right is for the NAVFLIR, and SCS Press/Depress (confusingly called "Down" in the manual and elsewhere) 1x is for the NAVFLIR and 2x for the TPOD.
- The sensor your TDC is actually controlling is usually shown in the top left of the right MFD (TV/INS for the DMT, IRMV for Mavs, or TPOD for TPOD).