305 - Flight - Navigation and Waypoints

Harrier has up to 60 Waypoints (W1-W60, each with an Offset point), 30 Markpoints (MK0-MK29), and some number of Targetpoints (T0-??). T0 is generally the last place you fired a weapon at.

Basic Navigation
Waypoints, Markpoints, and Targetpoints
1. Press Lower Gray Button (WINC/Waypoint Increment) to cycle through your currently selected point type (Waypoints, Markpoints, or Targetpoints), or use Waypoint Inc/Dec OSBs on ESHD page. Long-press the Waypoint Inc/Dec OSBs to skip to next category (waypoint/markpoint/targetpoint)??
2. To change the type of point you have selected, Long-press Lower Gray Button to open the Quick Access Menu on the UFC ODU, then select WYPT, MKPT, or TGPT, optionally enter the number of point you want to select on the UFC keyboard, and press ENT. Now pressing Lower Gray Button will cycle through that type of point.
TACAN
1. Press TCN button on UFC.
2. Enter TACAN channel number on keypad and press ENT.
3. Press ON/OFF to turn TACAN on.
4. On the Option Display Unit (left of UFC, above left MFD), select X or Y to set the channel letter, and T/R for land-based or carrier navigation, or A/A for air refueling tankers.
5. On EHSI page, TACAN bearing and range shows in the upper left corner. Press TCN button to put the steering info in the HUD (NAV master mode only??).

Create a new waypoint or Edit a waypoint by entering coordinates
1. On EHSD page, press DATA OSB to box.
2. On UFC keypad, enter number of waypoint to be created or edited, or 77 to create a new waypoint after the last one, then ENT. (New waypoint number will be shown with "*" on display.)
3. Enter the waypoint coordinates as either lat/long or MGRS:
Using latitude/longitude:
    1. Press POS UFC OSB (subsequent presses toggle between lat and long).
    2. Press 2 for N or 8 for S, then latitude in DDMMSS format, then ENT.
    3. Press 4 for W or 6 for E, then longitude in DDDMMSS format (note leading zero if needed), then ENT.
Using MGRS grid:
    1. Press UTM UFC OSB to show surrounding grids on other OSBs (subsequent presses show more surrounding grid squares).
    2. Select grid square by pressing corresponding UFC OSB.
    3. Enter coordinates on UFC keypay and press ENT.
1. Altitude is automatically set to ground level, change if needed by pressing the ALT OSB??
2. On EHSD page, press DATA OSB to unbox and stop editing.

Edit a waypoint by slewing the EHSD map -- WIP (organization)
1. On EHSD page, press DATA OSB to box.
2. Press POS UFC OSB.
3. Press Dish Hat forward to set TDC to INS.
4. Press SCL OSB to unbox and set desired zoom. Slew moves faster when zoomed out, slower when zoomed in.
5. Use TDC slew to move the waypoint on the EHSD map. All movement is saved immediately!
6. On EHSD page, press DATA OSB to unbox and stop editing.

Waypoint offsets, useful if you know a target bearing and distance from a waypoint
1. On EHSD page, press DATA OSB to box.
2. Press WYPT UFC OSB to change to WO/S (Waypoint OffSet).
3. Press BRG UFC OSB, then enter bearing on keypad, then ENT.
4. Press RNG UFC OSB, then enter range on keypad, then ENT. Numbers less than 100 are interpreted as nmi, numbers greater than 100 are interpreted as meters.
5. On EHSD page, press DATA OSB to unbox and stop editing.
6. Now when you have the waypoint with the offset selected, press the WO/S OSB to box it and track the offset instead of the waypoint itself.

Create Markpoint
1. Press MKn OSB on EHSD page. Creates Markpoint on the ground at your current aircraft location. MK1 stores in Markpoint 1, etc.
2. Or:
  1. Designate a target with TPOD or DMT.
  2. Press TOO button on UFC, select MKPT on UFC ODU, then enter a Markpoint number (next available number will be preselected), press ENT.

Create Targetpoint
1. Designate a target with TPOD or DMT.
2. Press TOO button on UFC, enter a Targetpoint number (next available number will be preselected), press ENT.