306 - Flight - Markpoints, Targetpoints, Jettison, Countermeasures

General info about Waypoints, Markpoints, and Targetpoints
- Waypoints ... W0-W60, W0 is your starting location
- Markpoints ... M0-M29
- Targetpoints ... T0-??, T0 is a special system targetpoint:
  - T0 is automatically updated to the aimpoint (CCIP point, rocket pipper point, etc.) when a weapon is fired.
  - Long-press Lower Gray Button to set T0 to the current designated point in the TPOD, and select it as the navigation destination. That also brings up the Quick Access Menu on the UFC ODU to select between the types of points.

Cycling/incrementing through Waypoints, Markpoints, and Targetpoints
- Press Lower Gray Button (WINC/Waypoint Increment) to cycle through your currently selected point type (either waypoints, markpoints, or targetpoints).
- Long-press Lower Gray Button to open the Quick Access Menu on the UFC ODU, then select WYPT, MKPT, or TGPT, optionally enter the number of point you want to select on the UFC keyboard, and press ENT. Now pressing Lower Gray Button will cycle through that type of point.
- Note: On EHSD page, when DATA is boxed, waypoint up/down arrows increment through all point types, but this is for display/editing them, and doesn't change your active navigation selection.

Create Markpoint
1. Press MKn OSB on EHSD page. Creates Markpoint on the ground at your current aircraft location. MK1 stores in Markpoint 1, etc.
2. Or:
  1. Designate a target with TPOD or DMT.
  2. Press TOO button on UFC, select MKPT on UFC ODU, then enter a Markpoint number (next available number will be preselected), press ENT.

Create Targetpoint
1. Designate a target with TPOD or DMT.
2. Press TOO button on UFC, enter a Targetpoint number (next available number will be preselected), press ENT.

Using T

How to use Mark Points and Target Points -- TODO
- Create Markpoints by pressing the MKn OSB (B2) at the bottom of the EHSI page, or the TOO button on the UFC.
- Markpoints can be your aircraft's current position, or a targeting pod coordinate??
- Press WPINC button long (Lower Gray Button long press) to set T0 as your navigation destination.

Import F10 map markers -- WIP, not sure exactly how this works...
1. Put marks on the map, labeled "#TP1", "#TP2", etc. "#TP01" etc. also works.
2. On right MFD, go to Menu > CAS > RCALL.
3. Press RShift-RAlt-8 to import targets from map.
  - Imported targets can be seen on built-in kneeboard page?? Doesn't seem to show anything has been imported... This may only show if marks are imported on the ground? Ground import should also automatically create target points, needs testing.
  - If marks are imported while airborne, they will be imported in the order they were made, regardless of #TPnn numbers.
  - NOTE: If you delete a marker and re-create it with the same name, and import again, it will show up as a new import. Imported marks can be deleted from the RCALL page by pressing the ERAS OSB on the UFC ODU.
  - For your own organization, it's recommended to name the #TPnn map markers in order from the next available item in the CAS > RCALL page.
1. Use up/down arrow OSBs to select one.
2. Press CAS OSB again, then press USE OSB.
3. On UFC, press number of target point you want to assign the mark to (e.g. 1), then ENT.
  - Enter more in sequence by repeating: Down arrow OSB, USE OSB, press number of target point (e.g. 2), then ENT.
1. Left MFD on EHSD screen will automatically go to DATA mode. If you move the TDC while in this mode, it will move the waypoint! Reimport the marker as that target point to reset (any other way to reset to original position??).
2. When finished importing and setting target points, press DATA OSB on left MFD.
3. Select Targetpoint

Jettison
1. Emergency Jettison button (black and yellow striped, far outboard) drops everything except A2A missiles.
2. Selective Jettison knob on Armament Control Panel does regular jettison. Set knob sleeve to desired category, then press center red JETT button.
  - STA = Individual stores selected with small round buttons under station numbers, also drops ejector racks.
  - STOR = Same as STA but keeps ejector racks.
  - SAFE = No jettison.
  - CMBT = Everything but A2A missiles, including ejector racks (same as Emergency Jettison button).
  - FUEL = External tanks.

Countermeasures programs -- WIP
1. Countermeasures can be programmed by going to the EW page (Menu OSB, EW OSB or Dish Hat Left 3x) and pressing PROG OSB.
2. Settings are changed with UFC OSBs??