202 - Ground - Preflight, Performance Limits

Preflight (after cold start or from hot start)
1. INSTRUMENTS and CONSOLES lights ... As desired (right console forward)
2. External lights ... As desired (right console forward)
3. Radar Altimeter ... Set bug as desired??
4. PITOT HEAT button ... As needed (left front wall, under gear handle)
5. ENGINE ANTI-ICE button ... As needed (ENGINE panel, left console in front of throttle
6. Radios ... As needed (see other page for radio tuning)
7. Navigation ... As needed (see other page for navigation systems)

Performance limits
- Fuel: 3960 lbs internal
- Fuel flow (sea level, ISA):
  - Mil power: approx 2000 lbs/hr
  - MPR power: approx 2600 lbs/hr
- Endurance:
  - Mil power: 1h59m
  - MPR power: 1h31m
- TFE731-5-1J engine ITT (Inter-Turbine Temperature):
  - The engine is robust and can be run at any attainable temperature for any length of time, including MPR power. Official real-life limit for MPR is 5 minutes, but pilots say that can be ignored.
- Engine oil:
  - 30 deg C, minimum
  - 127 deg C, max up to 30,000 ft
  - 149 deg C, max for 2 min at any altitude
- Flaps:
  - Takeoff: 190 kts
  - Full: 150 kts
- Landing gear: 200 kts
- Landing lights: 200 kts
- Zero or negative G flight: 30 sec
- Best climb speed: 215 kts at sea level clean, subtract 5 kts per 5000 ft (probably slower if heavier)
- Steepest climb speed: On-speed AOA (green circle in AOA meter)
- Tested max speed (sea level, ISA):
  - Clean/no pylons:
    - Mil power: 368 kts, Mach 0.56
    - MPR power: 381 kts, Mach 0.58
  - 2x AIM-9M and DEFA 30 mm cannon
    - Mil power: 328 kts, Mach 0.50
    - MPR power: 343 kts, Mach 0.52