302 - Flight - Radios, Flight Director, Jettison

Radios
COM1	VHF-20B	VHF	COMM: 116.000 to 151.975 MHz / NAV: 108.00 to 117.950 and 133.00 to 135.95	AM	"VHF-NAV" right console
COM2	V/TVU-740	VHF / UHF	118.000 to 149.975 MHz / 225.000 to 399.975 MHz	AM	"V/UHF" left instrument panel
--	ADF-60	??	190.000 to 1749.5 KHz	??	ADF receiver

Change active radio with large black knob on AUDIO panel (right console).
V/TVU-70 V/UHF radio
- V/UHF radio controls are on left side of front instrument panel.
- Power on by setting Function Dial to A3 or A3+G.
- Using presets:
  1. Frequency Mode Dial ... P (Preset)
  2. Change channel with Preset Channel Selector knob (black plus/cross knob). Channel is shown in display above, 21 channels available.
Changing preset channel frequencies:
Presets cannot be changed (as far as I can tell).
Manual frequency tuning:
1. Frequency Mode Dial ... M (Manual)
2. Set frequency with selector wheels.
VHF-20B VHF radio
- VHF radio controls are on right console.
- Power on by setting Power knob (outer ring of left knob) to ON (left/right click on knob)
- Manual frequency tuning (no presets available):
Set frequency with knobs (scroll up/down on knob)

Flight Director -- TODO
NOTE: Flight Director is not an autopilot, it just provides steering indicators.

Jettison -- TODO