401 - A/A - A/A guns and missiles

All weapons
1. On Optical Sight Control Unit panel (below gunsight):
  1. Power switch ... ON
  2. Mode switch ... MAN
    - NOTE: AUTO computes lead, but only at a fixed range?? manual is unclear, MAN mode is recommended.
  1. Gunsight depression ... 10 deg for centerline crosshair (Gray Reset Hat forward/back for tens, left/right for units)
2. On SCAR panel (bottom left instrument panel, above left knee):
  1. MAST SW ... ON

Guns -- M2 .50 cal MGs or DEFA 30 mm cannon
1. On SCAR panel (bottom left instrument panel, above left knee):
  1. Fixed Weapons Switch ... A/A (red guarded switch)
2. Release trigger safety catch (Flip-down Trigger press); front of stick grip will have a red bar exposed when safety is off.
3. Horizontal lines on pipper show 35 ft wingspan at various ranges:
┣━━ ┣━ ┣━ ⨀ ━┫ ━┫ ━━┫	= 700 ft / 233 yds / 213 m
      ┣━ ┣━ ⨀ ━┫ ━┫	= 1250 ft / 417 yds / 381 m
        ┣━ ⨀ ━┫	= 1800 ft / 600 yds / 549 m
┣━━ ⨀ ━━┫	= Snap Shot (not sure what this does??)
1. Adjust range with Top Hat Ring forward/back.
2. Aim with pipper, fire with Trigger.
  - SCAR Display Unit on top right of instrument panel shows rounds remaining.
- Wingspans:
  - MiG-29: 37 ft
  - F-16: 33 ft
  - Su-27: 48 ft
  - MiG-21: 24 ft
  - MiG-19: 30 ft
  - L-39: 31 ft

Missiles -- AIM-9M, AIM-9L, or Magic
1. On SCAR panel (bottom left instrument panel, above left knee):
  1. Weapon pylon buttons ... Select missile pylons (top light on button turns yellow when selected)
  2. MODE knob ... NC
2. Open stores release guard (Dish Hat up); stick grip will show safety guard up.
3. When you have tone, fire with Red Button. Left missile fires first.
- There is no ranging information, and the missile can lock well outside its effective range, so when in doubt, get closer.
- There is no cage/uncage.