501a - A/G - Guns, Unguided Bombs, Rockets, Sea Eagle ASM

Fence In
1. On Optical Sight Control Unit panel (below gunsight):
  1. Power switch ... ON
  2. Mode switch ... MAN
    - NOTE: AUTO computes lead, but only at a fixed range?? manual is unclear, MAN mode is recommended.
  1. Gunsight depression ... 10 deg for centerline crosshair, otherwise as needed, see below (Gray Reset Hat forward/back for tens, left/right for units)
2. On SCAR (weapons) panel (bottom left instrument panel, above left knee):
  1. MAST SW ... ON (B2 button)
  2. Fixed Weapons Switch ... A/G (red guarded switch to left of MAST SW) (B3/B6 button to open/close guard, B4 button for A/G mode)
3. Release trigger safety catch (Flip-down Trigger press); front of stick grip will have a red bar exposed when safety is off.
4. Open stores release guard (Dish Hat up); stick grip will show safety guard up.

Guns -- 2x M2 .50 cal MGs (220 rounds/gun) or 1x DEFA 30 mm cannon (130 rounds)
1. On SCAR panel (bottom left instrument panel, above left knee):
  1. Fixed Weapons Switch ... A/G (red guarded switch)
2. Gunsight depression ... 10 deg (Gray Reset Hat forward/back for tens, left/right for units)
3. Release trigger safety catch (Flip-down Trigger press); front of stick grip will have a red bar exposed when safety is off.
4. Aim with pipper, fire with Trigger.
  - SCAR Display Unit on top right of instrument panel shows rounds remaining per gun.

Rockets
1. On SCAR panel (bottom left instrument panel, above left knee):
  1. Weapon pylon buttons ... Select rocket pylons (top light on button turns yellow when selected)
  2. MODE knob ... ROC or BRST for single or ripple rockets respectively
    - 1-1 should be the correct setting for singles but doesn't work in the game. IRL, ROC would be used for a mixed launcher with both bombs and rockets.
1. Set gunsight depression (see tables on next page); 30 deg is a good default for steep dives or close range attacks (rocket motor still burning) (Gray Reset Hat forward/back for tens, left/right for units)
2. Open stores release guard (Dish Hat up); stick grip will show safety guard up.
3. Fire with Red Button.

Bombs
1. On SCAR panel (bottom left instrument panel, above left knee):
  1. Weapon pylon buttons ... Select bomb pylons (top light on button turns yellow when selected)
  2. ARM knob ... NS/TL, NS, or TL as needed
  3. MODE knob ... As desired:
    1. BOMB ... If single pylon is selected, only that bomb will be dropped. If multiple pylons are selected, bombs will drop in pairs from inboard, outboard, center in that order with each pickle.
    2. RIP ... Selected pylons are rippled with timing set by RIPPLE TIME knob.
  4. RIPPLE TIME knob ... As desired if using RIP mode (time in milliseconds):
Speed	70 ms	90 ms	120 ms	150 ms	200 ms
200	24 ft	30 ft	41 ft	51 ft	68 ft
250	30 ft	38 ft	51 ft	63 ft	84 ft
300	35 ft	46 ft	61 ft	76 ft	101 ft
350	41 ft	53 ft	71 ft	89 ft	118 ft
400	47 ft	61 ft	81 ft	101 ft	135 ft
450	53 ft	68 ft	91 ft	114 ft	152 ft

1. Set gunsight depression (see tables on next page) (Middle Finger Hat up/down for tens, left/right for units)
2. Open stores release guard (Dish Hat up); stick grip will show safety guard up.
3. Fire with Red Button.

Sea Eagle ASM
Sea Eagle target waypoint must be set in the Mission Editor. See Chuck's for details.
1. On SCAR panel (bottom left instrument panel, above left knee):
  1. Weapon pylon buttons ... Select Sea Eagle pylons (2 and 5) (top light on button turns yellow when selected)
  2. MODE knob ... ROC
2. Open stores release guard (Dish Hat up); stick grip will show safety guard up.
3. When within 60 nmi of the target, fire with Red Button.