202 - Ground - Preflight, Performance Limits

Preflight (after cold start or from hot start)
1. INSTRUMENTS and CONSOLES lights ... As desired (right console forward)
2. External lights ... As desired (right console forward)
3. PITOT HEAT button ... As needed (left front wall, under gear handle)
4. ENGINE ANTI-ICE button ... As needed (ENGINE panel, left console in front of throttle
5. Radios ... As needed (see other page for radio tuning)
6. Navigation ... As needed (see other page for navigation systems)
7. Smoke system (if equipped): White Smoke and Colour Smoke circuit breakers ... IN (left console outboard)

Performance limits
- Fuel: 3960 lbs internal
- Fuel flow (sea level, ISA)
  - Max continuous: approx 1580 lbs/hr
  - Mil power: approx 1680 lbs/hr
- Endurance on max continuous:
  - 100% fuel: 2h30m
  - 75% fuel: 1h52m
  - 66% fuel: 1h39m
  - 50% fuel: 1h15m
  - 33% fuel: 0h49m
  - 25% fuel: 0h37m
- TFE731-2-2J engine ITT (Inter-Turbine Temperature):
  - Takeoff power (5 min): 860 deg C
  - Mil power (30 mins): 796-832 deg C
  - Max continuous: 795 deg C
- Engine oil:
  - 30 deg C, minimum
  - 127 deg C, max up to 30,000 ft
  - 149 deg C, max for 2 min at any altitude
- Flaps:
  - Takeoff: 190 kts
  - Full: 150 kts
- Landing gear: 200 kts
- Landing lights: 200 kts
- Zero or negative G flight: 30 sec
- Best climb speed: 215 kts at sea level, subtract 5 kts per 5000 ft
- Tested max speed at sea level (50 ft) in ISA conditions, clean/no pylons:
  - Max continuous power: 355 kts, Mach 0.54
  - Full mil power: 367 kts, Mach 0.56